Engineering Severity Level Matrix

The Engineering Severity Level (ESL) matrix (Table 1), is a Dstl developed systems engineering tool used to capture an overview of the current and proposed future operational capability of prototype technology in regards to Defence and Security environments. The tool acts as a research aid for technology-to-platform down selection.

ESL	Climatic					Mechanical					Induced Electromagnetic (E.M.) Radiation
	Temperature			Humidity	Pressure			*Vibration		Acoustic	Un-mounted Shock	Tilt (degree)		†Electromagnetic Field			Magnetic Fields
	Min	Max	Rate /min	Relative	Min	Max	Rate /min	Peak Frequency	Peak Frequency Power Spectral Density	Noise	Peak	Max		Peak Frequency	Peak Strength	Avg Strength	Max	Rate/s
	°Celsius			% R.H.	kPa			Hz	g2/Hz	dBc	g	Degree	Degree /sec	Hz	Vm-1 peak	Vm-1 r.m.s.	G	G/s
8	-60	100	40	0-100	20	200	300	2000	0.0100	180	2000	360	1000	50G	10000	1000	5000	1000
7	-50	90	30	0-85	30	180	200	1500	0.0086	165	1000	300	500	18G	5000	800	1000	500
6	-40	80	20	0-70	40	160	100	1000	0.0074	150	500	240	250	6G	1000	600	100	100
5	-30	70	10	15-90	50	150	50	500	0.0061	135	100	190	100	1G	500	400	50	50
4	-20	60	5	15-70	60	140	10	250	0.0049	120	50	140	50	100M	200	200	25	25
3	-10	50	1	30-95	70	130	5	100	0.0036	105	30	90	10	70M	100	100	10	10
2	1	40	0.1	30-70	80	120	1	50	0.0024	90	10	30	1	30M	50	50	5	5
1	10	30	0.01	30-50	90	110	0.1	10	0.0011	75	5	15	0.1	500k	10	10	1	1
0	18	22	0	35-45	100	101	0	5	0.0001	60	1	1	0	10k	1	1	0.5	0.5

* Vibration: Peak acceleration power spectral density ESL value at the frequency ESL value stated.
† Electromagnetic (E.M.) Radiation: Peak and average field strengths at the EM peak frequency ESL value.

Table 1: Engineering Severity Level matrix

Suppliers will recognise that military platform environments are complex and involve a number of dependent parameters over a period of time. For simplicity purposes, the ESL matrix includes a range of independent environmental parameters, such as vibration dynamics, temperature, pressure, etc., that are indicative of a variety of military platforms in the Air, Sea and Land domain. Each environmental parameter increases in severity with each row, from a benign laboratory environment, ESL 0, to highly demanding operational environment, ESL 8.

Note that unlike real military platform environments, the ESL values represent a single event at an environmental parameter, hence a technology ESL matrix profile does not represent a life cycle engineering profile. Also, note that complex parameters, such as ionizing radiation environments, platform propulsion velocities and timescales, platform dynamics and excitation frequencies, have not been included. These complex environments will be discussed with suppliers at a later date.

Technology Size, Weight and Power Matrix

Other important aspects that are not captured in the ESL matrix are the physical dimensions and power requirements of the device. These can be very restrictive for a number of platforms. Table 2 is a matrix of typical Size Weight and Power (SWaP) constraints against military platform types. From left to right, the power requirements are increased, whereas from top to bottom the weight requirements are increased. These naturally define the size of device which increases diagonally from top left to bottom right. With the exception of the first column, the weight and size excludes the battery/generator itself.

	Power	Internal-battery powered	*Platform-battery powered	*Generator powered	*Mains powered
Weight
Lightweight and/or handheld		<1L, / <0.5W, / <1kg	<1L, / 1-50W, / <1kg
Backpack sized, person-portable		1-10L, / <1W, / 1kg - 10kg	1-10L, / 1-50W, / 1kg - 10kg	1-10L, / 50-1kW, / 1kg - 10kg	1-10L, / >1kW, / 1kg - 10kg
Rack mounted and vehicle portable		1-10L, / <1W, / 10kg - 50kg	10-100L, / 1-50W, / 10kg - 50kg	10-100L, / 50-1kW, / 10kg - 50kg	10-100L, >1kW, / 10kg - 50kg
Heavy, platform-fixed		1-10L, / <1W, / 50kg - 100kg	10-100L, / 1-50W, / 50kg - 100kg	100-1000L, / 50-1kW, / 50kg - 100kg	100-1000L, >1kW, / 50kg - 100kg
Very heavy, special mounting.				100-1000L, / 50-1kW, <1000kg	>1000L, / >1kW, <1000kg
* Degraded power quality should be expected and mitigated if necessary.

Table 2: Size, Weight and Power matrix

Mandatory Requirement 1: Current Technology ESL Matrix Capability Profile

Suppliers are required to assess the current operational environmental capability of the device’s physics package and driving devices[1], against the conditions stated in the ESL matrix (Table 1) and in conjunction with the defence and security Technical Readiness Level (TRL) definition, given in Appendix A.
[1] Physics package and driving devices includes all system components other than power generation, such as lasers, optics, acoustic optical modulators, amplifiers, etc.

In doing so, suppliers will submit a completed technology ESL matrix profile that reflects the current environmental operational capability (≥TRL 4) of the device against each environmental parameter, using the colours, indicated in Table 3.

Suppliers are required to comment against the completed technology ESL matrix profile in terms of technical performance capabilities for environmental conditions stated, assuming a single but repeatable event per parameter. It is anticipated that additional comments will be include on the expected degradation of performance of the physics package at specified ESL values and dependencies (such as initial GPS fix).

Example of a current technology ESL matrix profile, completed by a supplier, is given in Table 6.

Colour Key	Technology Capability	Description
Black	Inaccessible	The technology cannot operate under these conditions under any circumstance due to practical/technological/fundamental reasons.
Grey	Unknown	Best estimates should be given, but in cases where the response to the environment it truly unknown.
Amber	Current Survivable	The technology has been demonstrated (≥TRL 4) to survive under these conditions.
Green	Currently Operational	The technology has been demonstrated (≥TRL 4) to operate under these conditions.

Table 3: Current Technology ESL matrix profile colour coding key

Mandatory Requirement 2: Future Technology ESL Matrix Capability Profile

Suppliers are required to assess the future operational environmental capability of the device’s physics package and driving devices after ≤5 years of development, against the conditions stated in the ESL matrix (Table 1) and in conjunction with the defence and security TRL definition, given in Appendix A.

In doing so, suppliers will submit a second completed technology ESL matrix profile that reflects the potential future (≤5 year) operational capability (≥TRL 4) of the device against each parameter, using the colours, indicated in Table 4. Please note that the colours in Table 4 are identical to those in Table 3, but now represent the technologies capability after a 5 year development period.

Suppliers are required to comment on the second completed ESL matrix profile in terms of technical performance capabilities (≥TRL 4) for environmental conditions stated, assuming a single but repeatable event per parameter, and steps taken to progress the technology’s capability from the first ESL matrix profile to the proposed future ESL matrix profile.

It is anticipated that additional comments will include information on the expected degradation of performance of the physics package at specified ESL values, dependencies (such as initial GPS fix) and expected resources/financial commitments required to reach the future (≤5 year) stated ESL.

Example of a current technology ESL matrix profile, completed by a supplier, is given in Table 7.

Colour Key	Technology Capability	Description
Black	Inaccessible	The technology cannot operate under these conditions under any circumstance due to practical/technological/fundamental reasons.
Grey	Unknown	Best estimates should be given, but in cases where the response to the environment it truly unknown in a ≤5 year research period.
Amber	Near-term Survivable	The technology could be developed (≥TRL 4) and survive under these conditions in a ≤5 year research period.
Green	Near-term Operational	The technology could be developed (≥TRL 4) and operate under these conditions in a ≤5 year research period.

Table 4: Future technology ESL matrix profile colour coding key

Mandatory Requirement 3: Technology SWaP Development Matrix Profile

Suppliers are also required to assess the current and future (≤5 year) SWaP of the device against the technology SWaP matrix (Table 2). In doing so, suppliers will submit one completed technology SWaP matrix profile that reflects the current and future (≤5 year) SWaP of the device, described in the submitted technology ESL matrix profiles, using the different colour coding traffic light system, indicated in Table 5.

The process of using the technology SWaP matrix is identical to the ESL matrix. An example of a supplier generated technology SWaP development matrix profile for a device is given in Table 8.

Suppliers are required to comment against the completed technology SWaP development matrix profile in terms of technical capability and expected degradation of performance of the device’s physics package and driving components against the SWaP parameters. It is anticipated that additional comments will include information on required resources and financial commitment required to meet stated capability.

Colour Key	Capability	Description
Black	Impossible	By the fundamental nature of the technology it cannot fit within the SWAP category.

Grey	Unknown	Best estimates should be given, but in cases where their response to the environment is truly unknown in the near term (≤5 years).
Purple	Deliverable	The technology could be built within this category in the near term (≤5 years).

Orange	Current	The current form factor of the technology.

Table 5: Technology SWaP matrix development profile colour coding key

Example: Current and Future Technology ESL Matrix Profile

An example of a technology current and future ESL matrices profiles, as completed by a supplier for a device, are given in Table 6 and Table 7.
In the example: A TRL 4 prototype cold atom gyro is proposed by the contractor. Its current technology ESL profile (Table 6) indicates a device that can be delivered in the near term, is fragile and not particularly robust to vibrational noise. Moreover, its sensitivity to humidity is completely unknown outside of well-controlled laboratory conditions. However, the ESL matrix shown in Table 7, indicates that given the supplier stated resources over a 5 year period the physics package and driving elements could be developed to be quite resilient to moderate conditions across the ESL matrix.
ESL	Climatic					Mechanical					Induced Electromagnetic (E.M.) Radiation
	Temperature			Humidity	Pressure			*Vibration		Acoustic	Un-mounted Shock	Tilt (degree)		*Electromagnetic Field			Magnetic Fields
	Min	Max	Rate /min	Relative	Min	Max	Rate /min	Peak Frequency	Peak Frequency Power Spectral Density	Noise	Peak	Max		Peak Frequency	Peak Strength	Avg Strength	Max	Rate/s
	°Celsius			% R.H.	kPa			Hz	g2/Hz	dBc	g	Degree	Degree /sec	Hz	Vm-1 peak	Vm-1 r.m.s.	G	G/s
8	-60	100	40	0-100	20	200	300	2000	0.0100	180	2000	360	1000	50G	10000	1000	5000	1000
7	-50	90	30	0-85	30	180	200	1500	0.0086	165	1000	300	500	18G	5000	800	1000	500
6	-40	80	20	0-70	40	160	100	1000	0.0074	150	500	240	250	6G	1000	600	100	100
5	-30	70	10	15-90	50	150	50	500	0.0061	135	100	190	100	1G	500	400	50	50
4	-20	60	5	15-70	60	140	10	250	0.0049	120	50	140	50	100M	200	200	25	25
3	-10	50	1	30-95	70	130	5	100	0.0036	105	30	90	10	70M	100	100	10	10
2	1	40	0.1	30-70	80	120	1	50	0.0024	90	10	30	1	30M	50	50	5	5
1	10	30	0.01	30-50	90	110	0.1	10	0.0011	75	5	15	0.1	500k	10	10	1	1
0	18	22	0	35-45	100	101	0	5	0.0001	60	1	1	0	10k	1	1	0.5	0.5

* Vibration: Peak acceleration power spectral density ESL value at the frequency ESL value stated.
* Electromagnetic (E.M.) Radiation: Peak and average field strengths at the EM peak frequency ESL value stated.

Table 6: Example of a technology ESL matrix profile for a current device, completed by a supplier

ESL	Climatic					Mechanical					Induced Electromagnetic (E.M.) Radiation
	Temperature			Humidity	Pressure			*Vibration		Acoustic	Un-mounted Shock	Tilt (degree)		*Electromagnetic Field			Magnetic Fields
	Min	Max	Rate /min	Relative	Min	Max	Rate /min	Peak Frequency	Peak Frequency Power Spectral Density	Noise	Peak	Max		Peak Frequency	Peak Strength	Avg Strength	Max	Rate/s
	°Celsius			% R.H.	kPa			Hz	g2/Hz	dBc	g	Degree	Degree /sec	Hz	Vm-1 peak	Vm-1 r.m.s.	G	G/s
8	-60	100	40	0-100	20	200	300	2000	0.0100	180	2000	360	1000	50G	10000	1000	5000	1000
7	-50	90	30	0-85	30	180	200	1500	0.0086	165	1000	300	500	18G	5000	800	1000	500
6	-40	80	20	0-70	40	160	100	1000	0.0074	150	500	240	250	6G	1000	600	100	100
5	-30	70	10	15-90	50	150	50	500	0.0061	135	100	190	100	1G	500	400	50	50
4	-20	60	5	15-70	60	140	10	250	0.0049	120	50	140	50	100M	200	200	25	25
3	-10	50	1	30-95	70	130	5	100	0.0036	105	30	90	10	70M	100	100	10	10
2	1	40	0.1	30-70	80	120	1	50	0.0024	90	10	30	1	30M	50	50	5	5
1	10	30	0.01	30-50	90	110	0.1	10	0.0011	75	5	15	0.1	500k	10	10	1	1
0	18	22	0	35-45	100	101	0	5	0.0001	60	1	1	0	10k	1	1	0.5	0.5

* Vibration: Peak acceleration power spectral density ESL value at the frequency ESL value stated.
* Electromagnetic (E.M.) Radiation: Peak and average field strengths at the EM peak frequency ESL value stated.

Table 7: Example of a technology development ESL matrix profile for a future device, completed by a supplier
Example: Technology SWaP Matrix Development Profile

An example of a SWaP development matrix profile that complements the TRL 4 cold atom gyro ESL current and future matrices, completed by a supplier, is given in Table 8.
In the example, the supplier states that the bulk optics and cavity required must be a specific length and are relatively heavy, which puts a fundamental limit to the size and weight of the physics package. However, with research and development, it could be significantly miniaturised over 5 years using integrated optics and fibres. The physics package requires a 2W amplifier to drive an electro-optic component which in the near-term is considered to be a hard requirement within the technology - limiting the reduction in power required. The confidence of the supplier’s best estimate crosses several different weight/size categories.

Weight	Power	*Internal-battery powered	*Platform-battery powered	*Generator powered	Mains powered
Lightweight and/or handheld		<1L, / <0.5W, / <1kg	<1L, / 1-50W, / <1kg
Backpack sized, person-portable		1-10L, / <1W, / 1kg - 10kg	1-11L, / 1-50W, / 1kg - 10kg	1-10L, / 51-1000W, / 1kg - 10kg	1-10lt, / >1kW, / 1kg - 10kg
Rack mounted and vehicle portable		1-10L, / <1W, / 11kg - 50kg	11-100L, / 1-50W, / 11kg - 50kg	11-100L, / 51-1000W, / 11kg - 50kg	11-100L, >1kW, / 11kg - 50kg
Heavy, platform-fixed		1-10L, / <1W, / 51kg - 100kg	11-100L, / 1-50W, / 51kg - 100kg	101-1000L, / 51-1000W, / 51kg - 100kg	101-1000L, >1kW, / 51kg - 100kg
Very heavy, special mounting.				101-1000L, / 51-1000W, <1000kg	>1000L, / >1kW, <1000kg

Table 8 Example of Size, Weight and Power development matrix for a device, completed by a supplier

Appendix A - TRL Definitions, Descriptions and Supporting Evidence

TRL	Definition	System
		Description	Supporting Evidence
6	Technology system / sub-system model or prototype demonstration in a relevant environment	Representative model or prototype system, which is well beyond that of TRL5, is tested in a relevant environment. Represents a major step up in technology’s demonstration readiness. Examples include field testing a prototype in a high fidelity laboratory environments or in a simulated operational environment operating under proposed protocols.	Results from field testing of a prototype system that is near the desired configuration in terms of performance, weight and volume. How did the test environment differ from the operational environment? Who performed the tests? How did the test compare with expectations? What problems, if any, were encountered? What are the plans, options or actions to resolve problems before moving to the next level?
5	Technology component and/or basic technology subsystem validation in relevant environment.	Fidelity of technology increases significantly. The basic technological components are integrated with reasonably realistic supporting elements so they can be tested in a simulated environment. Examples include high fidelity laboratory integration of components, and basic field trials to prove capability concepts.	Results from testing a laboratory based system are integrated with other supporting elements in a simulated operational environment. How does the “relevant environment” differ from the expected operational environment? How do the test results compare with expectations? What problems, if any, were encountered?
4	Technology component and/or basic technology subsystem validation in laboratory environment.	Basic technological components are integrated as sub-systems to establish that they will work together. This is relatively low fidelity compared with the eventual system. Examples include integration of ad-hoc hardware in the laboratory.	System concepts that have been considered and results from testing laboratory scale models. References to who did this work and when. Provide an estimate of how hardware and test results differ from the expected system goals and (re)assess the way forward.