# Calculations used in monitoring discharges to water
This supports the Environment Agency guidance Monitoring discharges to water: guidance on selecting a monitoring approach.
## Equation 1: calculating a representative concentration over a longer time period

Where:
- Cw = flow weighted average concentration of the determinand
- n = the number of measuring periods
- ci = the average concentration of determinand during ith measurement period
- qi = the average flow rate during ith measurement period
## Equation 2: calculating a monthly or yearly average load based on a daily measurement frequency

Where:
- lspecific = the average specific load of the parameter
- n = the number of measuring periods
- ci = the average concentration of determinand during ith measurement period
- qi = the average flow rate during ith measurement period
- pi = the production output during ith measurement period (or raw material consumed)
## Equation 3: calculating the percentage of spiked determinand recovered

Where:
- U = measured concentration in unspiked sample
- S = measured concentration in spiked sample
- C = concentration of spiking solution
- W = volume of spiking solution added
- V = volume of sample to which spike is added