## Slide 1: Capacity Market
Outline Design – Work in Progress
May 2013

## Slide 2: Agenda
High-level design
Volume of capacity to procure
Auction design
Trading
Penalties/overdelivery payments
Payment model & settlement

## Slide 3: Capacity Market –high-level design
Capacity to procure
Auction
Trading
Delivery
Payment
Total amount of capacity contracted for from providers willing to provide it through a central auction
Includes DSR, storage etc as well as generation
Limited physical trading (novation) of obligations
Capacity providers may hedge their position in private markets
Providers of capacity commit to be available when needed or face penalties in the delivery year
Capacity Market does not replace the energy market
Costs of capacity shared between suppliers, in proportion to their share of system peak demand
Enduring Reliability Standard established by Government
SO forecasts peak demand and translates into a capacity requirement
Implementation
Bodies have clear roles and responsibilities
Capacity Market can evolve as necessary
The material in this presentation is work in progress and is not a statement of Government policy or policy intent

## Slide 4: Deciding the volume of capacity to procure
Minded to run the first auction in 2014, for delivery of capacity in the winter of 2018/19
Ministers will set enduring reliability standard and a method for establishing a demand curve
Ministers will decide volume of capacity to procure, on basis of advice, using reliability standard and demand curve
Quantity required procured through auctions 4 years ahead and 1 year ahead (for DSR)
Successful bidders can participate in National Grid administered STOR tenders
Process intended to be as mechanistic as possible, while enabling costs to be controlled
The material in this presentation is work in progress and is not a statement of Government policy or policy intent

## Slide 5: Auction
Auction type:
Pay-as-clear descending clock auction with downward sloping demand curve (to enable trade-off between cost and volume)
Eligibility:
Eligible: Generation (inc CHP), Demand Side Response, Storage
Ineligible: CfD plant while CfD administratively set, RO plant, interconnected capacity
The material in this presentation is work in progress and is not a statement of Government policy or policy intent
Pre-Qualification:
All participants have to pre-qualify
Plant de-rating factors set by SO
Existing plant wishing to be “price makers” need to produce supporting evidence
Offers in auction:
Price, Capacity, Term (£/MW, MW, Term)
Different contract lengths available – e.g. 1 year for existing, 10 years for new, 3 years for refurbished

## Slide 6: Trading
Obligations can be physically traded (novation) from the year ahead of a delivery year
SO’s consent to each trade required; trading parties’ eligibility and pre-qualification status assessed
Plant able to take on additional obligations include:
  Plant unsuccessful in auction
  New plant commissioned early
  Capacity pre-qualified but didn’t participate in auction
Registry platform for capacity obligations
Plant with existing capacity obligations, opted out plant or retiring plant will not be able to take on additional obligations
All plant able to hedge their positions financially in private markets
The material in this presentation is work in progress and is not a statement of Government policy or policy intent

## Slide 7: Definition of product / penalties & overdelivery payments
Stress event defined as the issue/rescinding of demand control instructions by SO to DNOs
Delivery defined as lower of metered output or FPN plus SO’s instructions
‘VoLL-cash out’ based penalty rate for providers failing to deliver as per their obligation; overdelivery paid at the same rate
Ex-post assessment of obligation and delivery
Penalty liability is capped on portfolio-wide basis
Light touch physical checking regime
Penalties/overdelivery payments only where stress event preceded by ‘Capacity Market Warning’ at least four hours in advance
Changes in delivery in periods of stress between warning and elapse of four hour period rewarded/penalised
The material in this presentation is work in progress and is not a statement of Government policy or policy intent

## Slide 8: Payment Model and Settlement
Requirement on industry participants to meet financial commitments
  All licensed generators and suppliers [and aggregators] required to accede
  Capacity Instruments issued to successful bidders
Settlement body has right of Cost Recovery (including administration fees & the approved costs of its agents)
  Costs recovered from suppliers according to proportion of system peak demand
  Surplus/shortfall distributed/collected from suppliers (following year)
Billing Period – monthly
Collateral required from suppliers
Work on flow-through of penalties to affected customers
The material in this presentation is work in progress and is not a statement of Government policy or policy intent

## Slide 9
Thank you for your time
Any questions
?