MOD FORM 2206

ELECTRICAL INSTALLATION PERIODIC VISUAL INSPECTION RECORD SHEETS

| Site: | Building: |
| --- | --- |
| OUTCOMES | Acceptable condition | ( | Unacceptable condition | State C1 or C2 | Improvement recommended | State C3 | Not verified | N/V | Limitation | LIM | Not applicable | N/A |
| ITEM NO | DESCRIPTION | OUTCOME (Use codes above. Provide additional comment where appropriate. C1, C2 and C3 coded items to be recorded in Section K of the Condition Report) | Further investigation required? (Y or N) |
| 1.0 | DISTRIBUTOR’S / SUPPLY INTAKE EQUIPMENT |  |  |
| 1.1 | Service cable condition |  |  |
| 1.2 | Condition of service head |  |  |
| 1.3 | Condition of tails - Distributor |  |  |
| 1.4 | Condition of tails - Consumer |  |  |
| 1.5 | Condition of metering equipment |  |  |
| 1.6 | Condition of isolator (where present) |  |  |
| 2.0 | PRESENCE OF ADEQUATE ARRANGEMENTS FOR OTHER SOURCES SUCH AS MICRO GENERATORS (551.6; 551.7) |  |  |
| 3.0 | EARTHING / BONDING ARRANGEMENTS (411.3; Chap 54) |  |  |
| 3.1 | Presence and condition of distributor’s earthing arrangement (542.1.2.1; 542.1.2.2) |  |  |
| 3.2 | Presence and condition of earth electrode connection where applicable (542.1.2.3) |  |  |
| 3.3 | Provision of earthing / bonding labels at all appropriate locations (514.13) |  |  |
| 3.4 | Confirmation of earthing conductor size (542.3; 543.1.1) |  |  |
| 3.5 | Accessibility and condition of earthing conductor at MET (543.3.2) |  |  |
| 3.6 | Confirmation of main protective bonding conductor sizes (544.1) |  |  |
| 3.7 | Condition and accessibility of main protective bonding conductor connections (543.3.2; 544.1.2) |  |  |
| 3.8 | Accessibility and condition of all protective bonding connections (543.3.2) |  |  |
| 4.0 | CONSUMER UNIT(S) / DISTRIBUTION BOARD(S) |  |  |
| 4.1 | Adequacy of working space / accessibility to consumer unit / distribution board (132.12; 513.1) |  |  |
| 4.2 | Security of fixing (134.1.1) |  |  |
| 4.3 | Condition of enclosure(s) in terms of IP rating etc (416.2) |  |  |
| 4.4 | Condition of enclosure(s) in terms of fire rating etc (526.5) |  |  |
| 4.5 | Enclosure not damaged/deteriorated so as to impair safety (621.2(iii)) |  |  |
| 4.6 | Presence of main linked switch (as required by 537.1.4) |  |  |
| 4.7 | Operation of main switch (functional check) (612.13.2) |  |  |
| 4.8 | Manual operation of circuit-breakers and RCDs to prove disconnection (612.13.2) |  |  |
| 4.9 | Correct identification of circuit details and protective devices (514.8.1; 514.9.1) |  |  |
| 4.10 | Presence of RCD quarterly test notice at or near consumer unit / distribution board (514.12.2) |  |  |
| 4.11 | Presence of non-standard (mixed) cable colour warning notice at or near consumer unit /distribution board (514.14) |  |  |

Inspected by:

Name (Capitals) ………………………………………………..

Signature ……………………………………………................

Date ……………………………………………........................

| Site: | Building: |
| --- | --- |
| 4.12 | Presence of alternative supply warning notice at or near consumer unit / distribution board (514.15) |  |  |
| 4.13 | Presence of other required labelling (please specify) (Section 514) |  |  |
| 4.14 | Examination of protective device(s) and base(s); correct type and rating (no signs of unacceptable thermal damage, arcing or overheating) (421.1.3) |  |  |
| 4.15 | Single-pole protective devices in line conductor only (132.14.1; 530.3.2) |  |  |
| 4.16 | Protection against mechanical damage where cables enter consumer unit / distribution board(522.8.1; 522.8.11) |  |  |
| 4.17 | Protection against electromagnetic effects where cables enter consumer unit / distribution board /enclosures (521.5.1) |  |  |
| 4.18 | RCD(s) provided for fault protection – includes RCBOs (411.4.9; 411.5.2; 531.2) |  |  |
| 4.19 | RCD(s) provided for additional protection - includes RCBOs (411.3.3; 415.1) |  |  |
| 5.0 | FINAL CIRCUITS |  |  |
| 5.1 | Identification of conductors (514.3.1) |  |  |
| 5.2 | Cables correctly supported throughout their run (522.8.5) |  |  |
| 5.3 | Condition of insulation of live parts (416.1) |  |  |
| 5.4 | Non-sheathed cables protected by enclosure in conduit, ducting or trunking (521.10.1) |  |  |
|  | To include the integrity of conduit and trunking systems (metallic and plastic) |  |  |
| 5.5 | Adequacy of cables for current-carrying capacity with regard for the type and nature of installation (Section 523) |  |  |
| 5.6 | Coordination between conductors and overload protective devices (433.1; 533.2.1) |  |  |
| 5.7 | Adequacy of protective devices: type and rated current for fault protection (411.3) |  |  |
| 5.8 | Presence and adequacy of circuit protective conductors (411.3.1.1; 543.1) |  |  |
| 5.9 | Wiring system(s) appropriate for the type and nature of the installation and external influences (Section 522) |  |  |
| 5.10 | Concealed cables installed in prescribed zones (see Section D. Extent and limitations) (522.6.101) |  |  |
| 5.11 | Concealed cables incorporating earthed armour or sheath, or run within earthed wiring system, or otherwise protected against mechanical damage from nails, screws and the like (see Section D. Extent and limitations) (522.6.101; 522.6.103) |  |  |
| 5.12 | Provision of additional protection by RCD not exceeding 30 Ma: |  |  |
|  | for all socket-outlets provided for use within an electrostatic protected area. |  |  |
|  | for supply to mobile equipment not exceeding 32 A rating for use outdoors (411.3.3) |  |  |
|  | for cables concealed in walls or partitions (522.6.102; 522.6.103) |  |  |
| 5.13 | Provision of fire barriers, sealing arrangements and protection against thermal effects (Section 527) |  |  |
| 5.14 | Band II cables segregated / separated from Band I cables (528.1) |  |  |
| 5.15 | Cables segregated / separated from communications cabling (528.2) |  |  |
| 5.16 | Cables segregated / separated from non-electrical services (528.3) |  |  |
| 5.17 | Termination of cables at enclosures – indicate extent of sampling in Section D of the report (Section 526) |  |  |
|  | Connections soundly made and under no undue strain (526.6) |  |  |
|  | No basic insulation of a conductor visible outside enclosure (526.8) |  |  |
|  | Connections of live conductors adequately enclosed (526.5) |  |  |
|  | Adequately connected at point of entry to enclosure (glands, bushes etc.) (522.8.5) |  |  |
| 5.18 | Condition of accessories including socket-outlets, switches and joint boxes (621.2(iii)) |  |  |

Inspected by:

Name (Capitals) ………………………………………………..

Signature ……………………………………………................

Date ……………………………………………........................

| Site: | Building: |
| --- | --- |
| 5.19 | Suitability of accessories for external influences (512.2) |  |  |
| 6.0 | LOCATION(S) CONTAINING A BATH OR SHOWER |  |  |
| 6.1 | Additional protection for all low voltage (LV) circuits by RCD not exceeding 30 Ma (701.411.3.3) |  |  |
| 6.2 | Where used as a protective measure, requirements for SELV or PELV met (701.414.4.5) |  |  |
| 6.3 | Shaver sockets comply with BS EN 61558-2-5 formerly BS 3535 (701.512.3) |  |  |
| 6.4 | Presence of supplementary bonding conductors, unless not required by BS 7671:2008 (701.415.2) |  |  |
| 6.5 | Low voltage (e.g. 230 volt) socket-outlets sited at least 3 m from zone 1 (701.512.3) |  |  |
| 6.6 | Suitability of equipment for external influences for installed location in terms of IP rating (701.512.2) |  |  |
| 6.7 | Suitability of equipment for installation in a particular zone (701.512.3) |  |  |
| 6.8 | Suitability of current-using equipment for particular position within the location (701.55) |  |  |
| 7.0 | OTHER PART 7 SPECIAL INSTALLATIONS OR LOCATIONS |  |  |
| 7.1 | List all other special installations or locations present, if any. (Record separately the results of particular inspections applied.) |  |  |
| 8.0 | GENERAL |  |  |
| 8.1 | Presence and correct location of appropriate devices for isolation and switching |  |  |
| 8.2 | Adequacy of access to switchgear and other equipment |  |  |
| 8.3 | Particular protective measures for special installations and locations |  |  |
| 8.4 | Connection of single pole devices for protection in line/phase conductors only |  |  |
| 8.5 | Correct connection of accessories and equipment |  |  |
| 8.6 | Presence of undervoltage protective devices |  |  |
| 8.7 | Selection of equipment and protective measures appropriate to external influences |  |  |
| 8.8 | Selection of appropriate functional switching devices |  |  |
| 8.9 | Unauthorised modifications |  |  |
| 8.10 | Presence of diagrams, instructions, circuit charts and similar information |  |  |
| 8.11 | Presence of danger notices and other warning notices, including that they are securely fixed, durable and legible |  |  |
| 8.12 | Labelling of protective devices, switches and terminals |  |  |
| 8.13 | Identification of conductors |  |  |
| 8.14 | Required labels fitted at the point of connection to every earthing conductor, and earth electrode, the main equipotential bonding and the points of every bonding conductor to every extraneous conductive part. |  |  |
| 8.15 | Correct Functioning of Circuit Breakers |  |  |
| 8.16 | Correct Functioning of Relays |  |  |
| 8.17 | Correct Functioning of Switches |  |  |
| 8.18 | Correct Functioning of Push Buttons |  |  |
| 8.19 | Correct Functioning of Contactors |  |  |
| 8.20 | Correct Functioning of Meters |  |  |
| 8.21 | Correct Functioning of Instruments |  |  |
| 8.22 | Tightness of all Connections, including integrity of main and supplementary bonding. |  |  |
| 8.23 | Integrity of locks and seals |  |  |

Note: Numbers in brackets are reference to BS7671:2008(2011)

Inspected by:

Name (Capitals) ………………………………………………..

Signature ……………………………………………................

Date ……………………………………………........................

REMEDIAL ACTIONS ARISING FROM ELECTRICAL INSTALLATION PERIODIC VISUAL INSPECTION

| Site: | Building: |
| --- | --- |
| OBSERVATION | CLASSIFICATION CODE | Recommended remedial action | Date of Action Complete |

Completed by:

Name (Capitals) ………………………………………………..

Signature ……………………………………………................

Date ……………………………………………........................

Classification Codes

Each observation relating to a concern about the safety of the installation shall be attributed an appropriate Classification Code selected from the standard codes C1, C2 and C3 as follows:

Code C1	‘Danger present’ Risk of injury. Immediate remedial action required

Code C2	‘Potentially dangerous’ Urgent remedial action required

Code C3	‘Improvement recommended