­

60mph Speed Trials
REACTIVE - On-Road Trial Q&A M4 junctions 3 to 12

For info for press office: the type of on-road trial on the M4 section will be to increase the speed limit from 50mph to 60mph in the evenings and at weekends.

Key safety Messages: Ensuring safety as our first imperative
The on-road trials have been designed based on the following safety principles;
- All new 60mph scenarios undertake a robust risk assessment based on the GG104 requirements for safety risk assessments;
- We will upgrade infrastructure, such as barriers, wherever necessary to be effective at 60mph;
- We will continue working with our supply chain to understand their safety concerns and what we can do to mitigate these through the risk assessment process;
- We are respectful of the health and safety obligations placed on our supply chain as part of the Construction Design & Management Regulations 2015. We have been and will continue to work closely with the supply chain ahead of and during any on-road trial;
- We will suspend any on-road trial if we feel the safety of workers or customers is compromised.

Our long-term aspiration for speed limits at roadworks
We will design traffic management to the highest safe speed for the location. We will continue to use lower speed limits in roadworks where it’s appropriate to do so.

Q. Why is the 60mph speed limit not being used all the time?
A. There are a number of things we need to consider when deciding the appropriate speed limit through roadworks. On M4 junctions 3 to 12 we looked at the location, road layout and the works being undertaken but were unable to operate a permanent 60mph speed limit. However, we did carry out a detailed risk assessment and identified when it was appropriate to increase the speed limit, which included evenings and weekends. Road users tell us that they find a blanket approach to speed limits in roadworks inappropriate so this way we can vary the speed limit depending on what activity is taking place.

Q. What changes have been made to facilitate 60mph?
A. When carrying out road improvements it’s often necessary to install temporary traffic management to allow works to be completed safely. On M4 junction 3 to 12 we’ve looked at the location of the roadworks, the road layout and the work being undertaken and designed the traffic management to enable us to use a 60mph speed limit. This includes;
- Installing barriers and crash cushions that are tested for higher speed limits
- Ensuring appropriately sized working areas, lane widths, road markings and signage
Providing portable message signs so we’re able to provide additional information to customers at the roadside if required. For example to warn road users of any incidents or broken-down vehicles ahead.

Q. Why wasn’t the 60mph speed limit implemented at the same time as the scheme started?
A. There are a number of things we need to consider when deciding the appropriate speed limit through roadworks. Not all locations or work activities can accommodate higher speeds and road users tell us that they find a blanket approach to speed limits in roadworks inappropriate. The work currently being undertaken on M4 between junctions 11 and 12 has provided an opportunity to safely vary the speed limit in roadworks to either 50mph or 60mph. We carried out a detailed risk assessment before varying the speed and we will continue to monitor the road conditions carefully.

Q. Will the new 60mph speed limit be enforced?
A. The 60mph speed limit will be enforced in the same way as any other speed limit in roadworks. The onus is on drivers to abide by speed limits and drive to the road conditions at the time.

Q. Is 60mph a legal speed limit within roadworks?
A. 60mph is a legal speed limit to use within roadworks. When carrying out road improvements it’s often necessary to install temporary traffic management to allow works to be completed safely, and Department for Transport guidance states that the traffic management should be designed to the highest possible safe speed for the location and the works being undertaken.

Q. Are the rotating speed signs legal for use within roadworks?
A. The rotating speed signs, also called prism signs are legal for use within roadworks. The signs are designed and manufactured to comply with Department for Transport guidance and standards.

Q. The speed signs reduced from 60mph to 50mph whilst I was driving passed.  Will I be fined for speeding?
A. The speed limit will be enforced in the same way as any other speed limit in roadworks. The technology recognises when the speed limit changes and drivers will have the opportunity to respond to the change in the posted limit. This will ensure that no speeding fines are issued unlawfully.

Q. One of the rotating speed signs is showing a different speed limit to the other signs.
A. If one of the rotating speed signs is showing a different speed limit to the others then this is likely a result of a technical fault. The technology has been developed to quickly recognise if a fault has occurred and is being continually monitored. We’ve developed contingency plans for any fault that can’t be quickly rectified, including ensuring no speed penalties are issued unlawfully. With the remaining signs it should still be clear what the overall speed limit is. We ask drivers to pay attention to all signs and drive at an appropriate speed for the conditions.

Q. Why are other projects nearby not at 60mph?
Department for Transport guidance states that traffic management should be designed to the highest possible safe speed for the location and the works being undertaken. Each road improvement scheme is different, and the speed limit used through the roadworks will depend on the individual circumstances for that scheme. Although other road projects are not currently operating a 60mph speed limit through roadworks we are continuing to look for opportunities to safely increase the speed limit in the future.

Q. How can I provide feedback?
A. We always appreciate your feedback and there are a number of different ways for you to get in touch. If you’ve driven through the roadworks and would like to share your experience you can speak to one of our contact centre advisors on 0300 123 5000 or email us at info@highwaysengland.co.uk

-ends-