ministry of agriculture, fisheries and food	CSG 15

Research and Development

Final Project Report

(Not to be used for LINK projects)

Two hard copies of this form should be returned to: Research Policy and International Division, Final Reports Unit MAFF, Area 6/01 1A Page Street, London SW1P 4PQ An electronic version should be e-mailed to c.csgfinrep@csg.maff.gsi.gov.uk

| Project title | ABSOLUTE FIXING OF TIDE GAUGE BENCHMARKS BY GPS/GRAVIMETRY |
| --- | --- |

| MAFF project code | FD0305 |  |
| --- | --- | --- |

| Contractor organisation and location | PROUDMAN OCEANOGRAPHIC LABORATORY BIDSTON OBSERVATORY BIRKENHEAD CH43 7RA |
| --- | --- |

| Total MAFF project costs | £ 528,000 |  |
| --- | --- | --- |

| Project start date | 01/04/97 |  | Project end date | 31/03/00 |
| --- | --- | --- | --- | --- |

Executive summary (maximum 2 sides A4) To tab in this section press the tab key and the Control key together Press the DOWN arrow once to move to the next question.

The sea level rise trends around the British Isles consist of 2 components: the climate related changes in mean sea levels and the vertical movements of the land. The tide gauges in the National Tide Gauge Network measure the sea level relative to a local tide gauge bench-mark (TGBM). Thus a measured rise in mean sea levels can be due to the effects of climate change or it can be due to subsidence of the land at the TGBM (due to very local or regional subsidence or larger scale processes). In practice, the climate related component and the land movement component are of a similar order of magnitude at most sites and therefore it is important to measure the vertical land movements, so that these effects can be separated. In this project the new advanced geodetic techniques of GPS and absolute gravity are used to measure the land movements at a number of UK tide gauges. The improved knowledge and understanding of the variability of sea level changes around the coasts will provide important guidance for flood defence design.

In 1988 an international working group was set up in order to consider and make recommendations on the application of the developing geodetic techniques to the problem of geodetic fixing of TGBMs. In the working group report (Carter et al., 1989) the recommendation was made to regularly make episodic GPS (EGPS) measurements and absolute gravity measurements, in order to determine the vertical land movements at tide gauges. The target accuracy that the working group considered was necessary, in order to determine land movements to better than 1mm/year in a reasonable length of time, was 10mm for GPS in the vertical, and 20nm/sec² (2 (gals) for absolute gravity. Measuring the vertical velocity to 1mm/year, or better, is a major challenge both technically and because of various environmental signals that mainly affect only the vertical component. The working group therefore recommended that both GPS and absolute gravity measurements should be made, since this will allow an assessment of those error sources affecting the results at the 1mm/year level.

The report was very far sighted since the accuracies of GPS and absolute gravity were much worse at that stage and indeed it took a further 5 years before the target accuracies were achieved. In the early 1990s, GPS began to be deployed in permanent continuously operating (CGPS) networks for measuring horizontal tectonic movements in areas such as California and Japan. Further meetings of the international working group (Carter, 1994 and Neilan et al., 1997) recommended that CGPS should also be installed at tide gauges, whenever the resources are available, so that the vertical land movements could be determined in a shorter interval of time and so that environmental signals affecting the vertical could be better understood. Since the publication of these working group reports, several countries have started to measure land movements at tide gauges using a combination of permanent GPS, episodic GPS and absolute gravity measurements. The UK has been one of the leaders in the measurement of land movements at tide gauges and this report gives an overview of the progress and the main results obtained up to March 2000.

Permanent CGPS stations have been established at the tide gauges at Newlyn(1998), Liverpool(1999), Aberdeen(1998), Lowestoft(1999) and Sheerness(1997) and automated procedures developed for downloading and processing the data at the Institute of Engineering Surveying and Space Geodesy (IESSG), University of Nottingham. IESSG also made 2 sets of EGPS measurements at 12 other UK tide gauges using 3 ‘roving’ GPS receivers, in order to extend the series of EGPS measurements that have been made in earlier work and to develop a new monitoring strategy based on a combination of EGPS and CGPS measurements. The Proudman Oceanographic Laboratory (POL) made absolute gravity measurements at Newlyn, Lerwick and Aberdeen. The standard deviations of the daily height estimates from both the CGPS and EGPS measurements were in most cases of the order of 10mm or less. The standard deviations of the hourly gravity estimates were of the order of 2(gals.

It was clearly demonstrated that the new combined monitoring strategy gave improved height estimates for the EGPS stations i.e.fixing the coordinates of the UK CGPS stations relative to the International Terrestrial Reference Frame in the continuous GPS work, then enabled improved height agreements to be obtained at the EGPS stations.

The lengths of the various time series obtained up to the present means that most of the vertical station velocities are not yet statistically significant. For the tide gauges with CGPS, the most significant is for Sheerness, which has the longest time series (2.76 years). This shows an uplift of +3.6 ±2.0 mm/year. Repeated levellings between the Sheerness tide gauge and a reference benchmark on a fort 200 metres away show that there are some recent very local movements with the tide gauge apparently uplifting by about 2mm/year. For the EGPS tide gauge stations, vertical velocities have been determined for those with data spanning more than 8 years. Newhaven and Portsmouth both show some evidence of subsidence (vertical velocities of –1.5 ±0.9 and –1.1 ±0.6 mm/year respectively). The absolute gravity measurements at Newlyn show that gravity has changed by less than 1 (gal from 1995 to 2000, whereas at Lerwick there has been an increase of gravity of just over 2 (gals. For the vertical land movements, the gravity measurements give + 0.9 ±1.5mm/year for Newlyn and   -4.0 ±1.9mm/year for Lerwick. It should be noted that the Lambeck and Johnston (1995) geophysical model of the post-glacial rebound component of land movements predicts that the vertical land movements of Newlyn and Lerwick should be –1 mm/year and -2mm/year, respectively. The predicted subsidence at these 2 sites is mainly due to the so called hydro-isostatic subsidence caused by the long term viscous response of the Earth’s mantle to the loading from the increased mass in the oceans following the melting of the major ice sheets at the end of the last ice age.

The continuous GPS measurements show that there are systematic variations, most notably at annual time scales, which are coherent between all the stations. These systematic variations add to the uncertainty of the vertical trend estimates. Further research is required in order to understand the causes of these variations and to eliminate them from the time series.

A new research proposal has been submitted which will enable the lengths of the time series of CGPS, EGPS and absolute gravity measurements to be increased and thus to reduce the error bars on the vertical velocity estimates. In addition, new CGPS stations will be installed at 2 further tide gauges. The proposed research will also investigate the systematic variations in the height estimates and also investigate how the reliability of the estimated vertical land movements at tide gauges can be improved using a second inland CGPS station.

Scientific report (maximum 20 sides A4) To tab in this section press the tab key and the Control key together Press the DOWN arrow once to move to the next question.

GPS MEASUREMENTS

- Introduction

The scientific objectives of the research project were to set up a network for monitoring long term vertical land movements at sites of the UK National Tide Gauge Network using the Global Positioning System (GPS).  The deliverables for the research project were to be an established monitoring network, estimates of vertical land movements and recommendations on a strategy for long term monitoring.

This research project followed on from previous MAFF R&D projects (funded from 1990-1997 as FD0305:  The Geodetic Fixing of Tide Gauge Bench Marks).  In these earlier projects, episodic GPS campaigns were used for the geodetic fixing of tide gauge bench marks in the UK.  These campaigns were observed by using a large number of GPS receivers, deployed simultaneously for 5 days.  The episodic GPS data from stations in the UK were then processed along with data from stations in mainland Europe which form part of the International GPS Service (IGS) global GPS network.  Through these projects, extensive research and development was carried out on the systematic error models used for high precision GPS (Ashkenazi et al, 1994; Ashkenazi et al, 1997).

Over the last three years research has been concentrated on the development and testing of a new monitoring strategy based on a combination of continuous GPS data, observed using ‘continuously operating GPS receivers’ (COGRs) in the UK, and episodic GPS data observed by a ‘roving GPS receiver’.

Continuous GPS (CGPS) stations were established at the 4 tide gauge sites of Newlyn, Lowestoft, Liverpool and Aberdeen, and two sets of episodic GPS measurements were carried out at 12 other tide gauge sites in the UK.  The continuous GPS data from these 4 CGPS stations were supplemented by data from 5 more CGPS stations in the UK, which were installed as part of other IESSG research projects, and 4 IGS stations in mainland Europe.  This resulted in a monitoring network including 17 GPS stations (5 continuous and 12 episodic) at tide gauge sites in the UK.  The complete monitoring network is shown in Figure 1.

The new monitoring strategy was tested using continuous GPS data observed from March 1997 to December 1999 and episodic GPS data observed from May to December 1999.  Initial estimates of vertical land movements have been obtained for 5 CGPS stations in the UK, based on 1.7 to 2.7 years of continuous GPS data.  Furthermore, initial estimates of vertical land movements have been obtained for 4 episodic GPS (EGPS) stations located at tide gauge sites in the UK, based on 8 years of episodic GPS measurements, observed as part of this research project and as part of previous MAFF R&D projects.

The scientific objectives of the research project have been met in full.  Details of the methods used are given in section 2 and a discussion of the results obtained is presented in section 3.  The report is concluded in section 4, with the main implications of the findings, possible future work and recommended action resulting from the research.

## Figure 1  Network of Continuous GPS Stations and Episodic GPS Stations

2    Methodology

The methodology used for this research project can be separated into the establishment of the CGPS stations, the development of automated procedures for the remote operation of COGRs, the continuous GPS measurements, the episodic GPS measurements and the development of automated procedures for the processing and analysis of a combination of continuous and episodic GPS data.

2.1	Establishment of the CGPS Stations

When the research project began in April 1997, the IESSG had just established 4 CGPS stations.  One was at Nottingham, funded by the University, and three were in London, funded by the Environment Agency and NERC, as part of grant GR3/C0003
(Bingley et al, 1999).  One of these was the first CGPS station to be established at a site of the UK National Tide Gauge Network, in Sheerness.

In considering where to establish the 4 CGPS stations funded by MAFF, the primary objectives were to have a good geographical spread, to use tide gauges with long mean sea level (MSL) data sets and to establish CGPS stations in critical coastal zones.  The geographical spread was required for the testing of the new monitoring strategy, whereas the long MSL data sets would enable a comparison between MSL trends and estimates of current vertical land movements.  Hence, the tide gauge sites of Newlyn, Liverpool, Lowestoft and Aberdeen were selected.

Two significant international meetings took place in 1997, which also had a bearing on the establishment of the 4 CGPS stations funded by MAFF.  The first of these was a joint workshop of the IGS and the PSMSL which took place at the Jet Propulsion Laboratory in the USA.  The second was the initial meeting of Working Group 1 of the European Global Sea Level Observing System (EOSS), which is funded under European Commission COST Action 40.

Following the IGS / PSMSL workshop, the general consensus of opinion was that in order to monitor vertical land movement at a tide gauge site, for the purpose of decoupling this vertical land movement from changes in MSL measured by the tide gauge, the GPS antenna should be located on the same structure as, and as close to, the tide gauge as possible.  In order to take into account any extremely local variations in ground movement, such as local subsidence of the structure supporting the tide gauge, it was further recommended that a local stability network should be established to connect the CGPS station to other survey stations, up to a few kilometres away, sited on bedrock or ‘stable’ ground.  The EOSS Working
Group 1, went one step further than this and recommended that, ideally, one of the stations in the local stability network should be a second CGPS station, established on bedrock or ‘stable’ ground, inland from the tide gauge.

In April 1998, the IESSG established 4 CGPS stations at radiosonde sites for the UK Meteorological Office, three of which were relatively close to tide gauge sites, one in Camborne (about 20 km from Newlyn), one in Hemsby (about 20 km from Lowestoft) and one on the Shetland Isles (about 5 km from Lerwick).  Considering the recommendations of the IGS / PSMSL workshop however, it was clear that these CGPS stations were not close enough to be considered as monitoring the vertical land movement at the tide gauge itself.  As a result, it was decided to establish the 4 CGPS stations funded by MAFF at the tide gauge sites of Newlyn, Lowestoft, Liverpool and Aberdeen.

For each tide gauge site the necessary equipment was purchased, including an Ashtech Z-XII GPS receiver with Dorne-Margolin T (choke ring) antenna, and a modem.  Reconnaissances were then carried out in order to identify suitable locations for the GPS antenna, the GPS receiver and a telephone line.  Following the reconnaissances, permission was requested from the organisation responsible for the land and buildings on which the tide gauge is located.  Once the relevant permission was obtained, a survey monument was designed and manufactured for each site and a telephone line was installed at the site.  The installation of the monuments and GPS equipment were then carried out at Newlyn and Aberdeen in September 1998, and at Liverpool and Lowestoft in February 1999.

2.2	Automated Procedures for the Remote Operation of COGRs

For the previous MAFF R&D projects (funded as FD0305), episodic GPS campaigns were used for the geodetic fixing of tide gauge bench marks in the UK.  These campaigns were carried out by using a large number of GPS receivers, deployed simultaneously for 5 days and manned by surveyors responsible for their scheduling and downloading.  Unlike campaigns, a COGR is designed to observe continuous GPS data, 24 hours per day, 365 days of the year.  The move to using COGRs, therefore, leads to a significant change in the way that GPS data are observed and means that it must be possible to operate GPS receivers from a remote site and it must be possible to automate this operation.

Automated procedures for the remote operation of COGRs were first developed at the IESSG for use with the Trimble 4000 SSI GPS receivers established in London in March 1997.  For this research project these automated procedures were modified, for use with the Ashtech Z-XII GPS receivers installed at the tide gauge sites of Newlyn, Aberdeen, Liverpool and Lowestoft.  Using the automated procedures, daily observation data files are downloaded from the COGRs, via modems and standard telephone lines, and converted to RINEX (Receiver INdependent EXchange) format, which is suitable for input to the IESSG’s GAS GPS Analysis Software (Stewart et al, 1997).

2.3	Continuous GPS Measurements

The automated procedures described in section 2.2 were used to obtain continuous GPS data from the CGPS stations at Newlyn, Lowestoft, Liverpool and Aberdeen, and from the other 5 CGPS stations used in this research project, namely Sheerness, Nottingham, Camborne, Hemsby and Lerwick.

By the end of 1999, 16 months of continuous GPS data were available from Newlyn and Aberdeen and 11 months of continuous GPS data were available from Liverpool and Lowestoft.  This data is complemented by 33 months of continuous GPS data from Sheerness and Nottingham, and 21 months of continuous GPS data from Camborne, Hemsby and Lerwick.

The automated procedures developed for the remote operation of COGRs are extremely efficient and robust, resulting in about 99% of the continuous GPS data being successfully observed.  This is equivalent to a loss of only 2 to 4 days of data at each of the 4 CGPS stations funded by MAFF over their initial 11 to 16 month periods of operation.

2.4	Episodic GPS Measurements

In addition to the CGPS stations, the research project also included two sets of episodic GPS measurements at 12 other UK tide gauge sites.  These have been used to test the new monitoring strategy and to extend the height time series for those sites that were observed in previous MAFF R&D projects (Ashkenazi et al, 1994; Ashkenazi et al, 1997).

To fulfil the objectives, the two sets of episodic GPS measurements were not undertaken until the CGPS stations had been established at the tide gauge sites of Newlyn, Lowestoft, Liverpool and Aberdeen.  The first set of measurements was carried out from May to September 1999 and the second set was carried out from October to December 1999.  A summary of the episodic GPS measurements is given in Table 1, where the figures in brackets show the observation periods (in days x hours per day).

| Dates | ‘Roving’ GPS Receiver #1 | ‘Roving’ GPS Receiver #2 | ‘Roving’ GPS Receiver #3 |
| --- | --- | --- | --- |
| 09.05.99 to 16.05.99 | Stornoway (5 x 24) |  |  |
| 23.05.99 to 29.05.99 |  |  | Lerwick (5 x 12) |
| 20.06.99 to 26.06.99 |  | Millport (5 x 12) |  |
| 02.07.99 to 08.07.99 | Dover (5 x 24) | Newhaven (5 x 12) | Portsmouth (5 x 12) |
| 26.07.99 to 01.08.99 | Holyhead (5 x 24) | Heysham (5 x 12) |  |
| 09.08.99 to 15.08.99 | N Shields (5 x 24) | Immingham (5 x 24) | Portpatrick (5 x 12) |
| 20.09.99 to 26.09.99 |  |  | Avonmouth (5 x 12) |
| 24.10.99 to 31.10.99 | Stornoway (5 x 24) | Millport (5 x 12) | Lerwick (5 x 12) |
| 05.11.99 to 11.11.99 | Dover (5 x 24) | Newhaven (5 x 12) | Portsmouth (5 x 12) |
| 19.11.99 to 25.11.99 |  |  | Avonmouth (5 x 12) |
| 21.11.99 to 27.11.99 | Holyhead (5 x 24) | Heysham (5 x 12) |  |
| 06.12.99 to 12.12.99 | N Shields (5 x 24) | Immingham (5 x 24) | Portpatrick (5 x 12) |

Table 1  1999 Episodic GPS Measurements Summary

From Table 1 it can be seen that one, two or three ‘roving GPS receivers’ were used to make simultaneous episodic GPS measurements for 5 days at a ‘cluster’ of tide gauge sites.  Where possible, 24 hour GPS observations were made at the sites with sufficient security arrangements, with 12 hour GPS observations being made at the other sites.

2.4	Automated Procedures for Processing and Analysis

As stated in section 2.2, the use of continuous GPS data as part of the new monitoring strategy required a significant change in the way that GPS data are observed.  This also required a significant change in the treatment of GPS data during processing and analysis.

For the previous MAFF R&D projects (funded as FD0305), only episodic GPS campaigns were used for the geodetic fixing of tide gauge bench marks in the UK.  In this case, the episodic GPS data from the network of receivers in the UK were processed along with GPS data from a number of IGS stations in Europe.  This was carried out by so-called ‘manual processing’, which involved a great deal of user intervention and subjective decisions, particularly during the time consuming cycle slip detection and correction (cleaning) process.

The use of continuous GPS data increased the quantity of data processing required by two orders of magnitude, and basically meant that ‘manual processing’ was no longer an option.  Instead, it was necessary to refine the GAS GPS Analysis Software and develop procedures to enable ‘automatic processing’.  During this research project, the development and testing of automated procedures for processing and analysis have been well documented in the interim reports.  These developments resulted in three sets of automated procedures that were termed ‘Mark 1’, ‘Mark 2’ and ‘Mark 3’.

During the first twelve months of the research project, the ‘Mark 1’ automated procedures were developed.  The key development in the ‘Mark 1’ automated procedures was the definition of templates for the control files used in GAS.  These templates were designed to enable the automatic creation of control files through ‘stream editing’ and the insertion of time parameters, which are central to the majority of data management and file naming conventions used in GPS processing.

Over the next twelve months, a series of refinements were made to the ‘Mark 1’ automated procedures in order to improve the efficiency of cycle slip cleaning.  These developments led to the ‘Mark 2’ automated procedures, which attempted to automate the user intervention and subjective decisions associated with cycle slip cleaning when using GAS in a manual mode.

Following this, a series of refinements were made to the ‘Mark 2’ automated procedures in order to enable the processing of data from ‘noisier’ sites, which would traditionally have required more ‘expertise’ during cycle slip cleaning when using GAS in a manual mode.  The ‘Mark 3’ automated procedures are the result of a considerable amount of research and development that has been carried out over the last three years.  Throughout these developments a measure of the efficiency of the automated procedures has been obtained by considering the percentage of acceptable daily solutions produced for the CGPS stations, which represent a wide variety of environments in relation to their suitability for GPS signal reception.  This efficiency has gradually improved from an initial figure of about 60% at ‘good’ sites such as Nottingham, to the current level, where 95 to 98% of the observed data produces acceptable daily solutions at ‘good’ sites such as Nottingham and at ‘noisier’ tide gauge sites such as Aberdeen.

- Results

Using the ‘Mark 3’ automated procedures, it has been possible to generate a series of final results for the research project.  These are presented in this section, in terms of the continuous GPS stations and the episodic GPS stations.

3.1	Continuous GPS Stations

The continuous GPS data from the 4 CGPS stations funded by MAFF and the other 5 CGPS stations in the UK, have been processed along with data from the IGS stations at Onsala, Kootwijk, Wettzell and Villafranca.

The GPS data observed on a single day at all of these stations were processed in order to produce a ‘loosely constrained’ daily GPS network solution.  In these solutions, the IGS precise ephemeris was held fixed and the coordinates for Kootwijk were tightly constrained.  The coordinates for Kootwijk were taken from the same ITRF realisation as the IGS precise ephemeris.  Thus ITRF94 (Boucher et al, 1996) was used for solutions involving data collected between 26 March 1997 and 7 March 1998, ITRF96 (Boucher et al, 1998) for solutions involving data collected between 8 March 1998 and 31 July 1999, and ITRF97 (Boucher et al, 1999) thereafter.  In each case, the coordinates for Kootwijk were motioned to the observation epoch using the station velocity given in the appropriate ITRF realisation.

For all of the ‘loosely constrained’ daily GPS network solutions, the GPS data were processed using the L1/L2 ‘ionospherically free’ double difference observable with integer ambiguities not fixed, and a common set of systematic error models applied, including:

- corrections for Earth body tides (McCarthy, 1992).

- corrections for the M2, S2, N2, K2, K1, O1, P1, Q1, Mf and Mm (ie the constituents with semi-diurnal, diurnal, fortnightly and monthly periods respectively) for ocean tide loading (Baker et al, 1995), based on the FES941 model (Le Provost et al, 1994).

- corrections for antenna phase centre variations (Rothacher et al, 1995).

- modelling of the ‘dry’ zenith tropospheric delay using the Saastamoinen model (Saastamoinen, 1973), mapped to the appropriate station to satellite elevation angle using the Niell ‘dry’ mapping function (Niell, 1996).

- estimation of the ‘wet’ zenith tropospheric delay per station, as a random walk process using a process noise of 0.4 cm/sqrt(hr) (Dodson et al, 1996), mapped to the appropriate station to satellite elevation angle using the Niell ‘wet’ mapping function (Niell, 1996).

Following the processing, coordinate time series were formed for each of the CGPS stations.  In order to form coordinate time series with no discontinuities, the vectors and associated variance-covariance information output from each ‘loosely constrained’ daily GPS network solutions were transformed to a common reference frame.  This was carried out by tightly constraining Onsala, Kootwijk, Wettzell and Villafranca to their ITRF97 coordinates, motioned to the observation epoch.  Hence, the coordinate time series for the CGPS stations in the UK are represented in the ITRF97, based on daily coordinate estimates computed in the ITRF94, ITRF96 and ITRF97.

Figure 2 shows the ITRF97 daily height time series obtained for the CGPS stations, ordered in terms of the length of their time series and represented on an arbitrary scale for height.  Table 2 summarises the results obtained, in terms of the standard deviation of a daily height estimate from the time-averaged mean height for the 9 CGPS stations, and a vertical station velocity, with corresponding standard error, for the 5 CGPS stations with the longest time series.  The vertical station velocity is based on a linear regression and the estimates of standard error have been computed following Dixon (1991).

| CGPS Station | Time Series Length (years) | Height Standard Deviation (mm) | Vertical Station Velocity (mm/yr) |
| --- | --- | --- | --- |
| Sheerness | 2.76 | 10.9 | + 3.55 ± 1.95 |
| Nottingham | 2.70 | 8.2 | - 2.10 ± 1.52 |
| Camborne | 1.73 | 10.3 | - 0.34 ± 3.68 |
| Hemsby | 1.73 | 8.2 | - 1.90 ± 2.93 |
| Lerwick | 1.71 | 10.4 | - 0.35 ± 3.72 |
| Newlyn | 1.25 | 10.4 | - |
| Aberdeen | 1.29 | 14.0 | - |
| Liverpool | 0.90 | 8.9 | - |
| Lowestoft | 0.88 | 7.7 | - |

Table 2  CGPS Station Results Summary

The results confirm that it is possible to obtain a height standard deviation of about 10 mm when using continuous GPS data at CGPS stations in the UK, although it would appear that Aberdeen is a ‘noisier’ site, with a standard deviation of 14 mm.  Based on such relatively short time series, the standard errors obtained for the vertical station velocities confirm that these initial estimates of vertical land movements are not statistically significant, at this stage.

Figure 2  CGPS Station ITRF97 Daily Height Time Series

A closer inspection of the height time series given in Figure 2 indicates that there are variations in height which are not linear, but appear to follow an annual cycle with maxima in February and minima in July.  These variations are apparent at all of the CGPS stations, and add to the uncertainty of the vertical station velocities which assume a linear trend.

However, considering the trends in the vertical station velocities obtained for the 5 CGPS stations with the longest time series, there is a suggestion of subsidence at Nottingham and Hemsby, uplift at Sheerness and relatively little movement at Camborne and Lerwick.

The apparent uplift of the CGPS station at Sheerness is equivalent to about 10 mm over the last 2.76 years.  This is supported by further evidence from precise levelling which was undertaken between the Sheerness tide gauge and the tide gauge bench mark (TGBM), which is located on a fort about 200 m away.  Repeated levellings carried out in 1991 and 1995 also suggested that the small pier which supports the tide gauge building had risen by 10 mm relative to the TGBM, over a four year period.  Using MSL data for Sheerness from 1901 to 1996 Woodworth et al (1999) obtained a MSL trend of +2.14 ± 0.15 mm/yr.  Taking the IPCC’s estimate that global sea level has risen by 10 to 20 cm (or 1.5 mm/yr on average) over the last century, a simple estimate for the magnitude of local vertical land movement based on the MSL trend at Sheerness would be -0.64 mm/yr.  This is not consistent with the GPS estimate of +3.55 mm/yr, which suggests that the tide gauge has experienced significantly different vertical land movement over the last few years, most likely due to engineering type movements of the small pier which supports the tide gauge.

The results for the CGPS station at Sheerness are the first ‘real’ confirmation of the need to monitor current vertical land movements at tide gauge sites in the UK using high precision GPS.  The height standard deviations obtained for the 4 CGPS stations funded by MAFF are consistent with those obtained for Sheerness and confirm that it will be possible to obtain an assessment of vertical land movements at these tide gauge sites with longer time series.

3.2	Episodic GPS Stations

The GPS data from the 12 EGPS stations have been processed along with the data from 4 CGPS stations in the UK and the IGS stations at Onsala, Kootwijk, Wettzell and Villafranca, to produce another series of ‘loosely constrained’ daily GPS network solutions.  The 4 CGPS stations in the UK were Sheerness, Nottingham, Camborne and Lerwick, which were selected as being those with the longest time series, which provide a good geographical spread over the UK.  In these solutions, the IGS precise ephemeris was held fixed and the coordinates for Kootwijk were tightly constrained in the same way as described in section 3.1.  Furthermore, the same systematic error models were used, as detailed in section 3.1.

Following the processing, the daily height estimates for each specific five day period of episodic GPS data were combined in order to produce two independent epochal height estimates for each of the EGPS stations ie 99A and 99B.  These epochal height estimates were computed using two different approaches.  In the first approach these were computed by tightly constraining Onsala, Kootwijk, Wettzell and Villafranca to their ITRF97 coordinates, motioned to the observation epoch.  However, in the second approach, these were computed by tightly constraining Sheerness, Nottingham, Camborne and Lerwick to their ITRF97 coordinates, obtained from the continuous GPS data as detailed in section 3.1.

A comparison of the two approaches is given in Table 3, based on the height standard deviations and the height agreement (ie 99B minus 99A) between the two sets of episodic GPS measurements.

| EGPS Station | 4 IGS Stations Fixed | 4 UK CGPS Stations Fixed |
| --- | --- | --- |
|  | 99A SD | 99B SD | 99B-99A | 99A SD | 99B SD | 99B-99A |
| Portsmouth | 5.1 | 1.6 | +12.5 | 7.2 | 2.6 | +7.8 |
| Newhaven | 4.1 | 5.3 | +11.3 | 4.3 | 4.2 | +6.7 |
| Dover | 1.1 | 2.3 | +5.2 | 4.7 | 2.8 | +0.9 |
| Avonmouth | 4.5 | 7.1 | +4.6 | 5.6 | 5.4 | +8.8 |
| Holyhead | 2.6 | 7.4 | +3.8 | 2.2 | 4.6 | +7.3 |
| Immingham | 6.8 | 4.0 | +18.8 | 4.2 | 5.6 | +9.3 |
| Heysham | 2.9 | 7.9 | +7.2 | 6.3 | 9.0 | +7.3 |
| Portpatrick | 6.6 | 1.2 | +26.7 | 4.1 | 2.7 | +15.2 |
| N Shields | 7.0 | 3.6 | +22.5 | 5.1 | 3.8 | +9.7 |
| Millport | 4.6 | 2.0 | +11.5 | 5.2 | 7.3 | +11.1 |
| Stornoway | 4.0 | 2.8 | -5.2 | 3.1 | 7.0 | -4.1 |
| Lerwick | 9.4 | 2.8 | +12.0 | 8.4 | 5.2 | +8.1 |

Table 3  Monitoring Strategy Constraints Test

The height agreements when the 4 IGS stations are fixed are comparable to those obtained when using episodic GPS campaigns (Ashkenazi et al, 1997).  However, it can clearly be seen that these height agreements are improved significantly at most EGPS stations when the 4 UK CGPS stations are fixed.  This is most likely due to improvements in the tropospheric modelling over the UK when coordinate constraints are applied on a smaller regional scale.  This is the first indication of the success of the new monitoring strategy, with the availability of CGPS stations in the UK improving the height estimates obtained for EGPS stations.

The two new epochal height estimates obtained for the 12 EGPS stations, based on the second approach to applying constraints, have been used in conjunction with previous height estimates (Ashkenazi et al, 1997) to form height time series for the period from 1991 to 1999. Figure 3 shows the ITRF97 epochal height time series obtained for the EGPS stations, ordered in terms of their latitude and represented on an arbitrary scale for height.  Table 4 summarises the results obtained.

Figure 3  EGPS Station ITRF97 Epochal Height Time Series

| EGPS Station | Time Series Length | Height Standard | Vertical Station |
| --- | --- | --- | --- |
|  | (years) | (epochs) | Deviation (mm) | Velocity (mm/yr) |
| Portsmouth | 8.25 | 7 | 4.9 | -1.08 ± 0.64 |
| Newhaven | 8.25 | 4 | 6.1 | -1.48 ± 0.94 |
| Dover | 8.25 | 8 | 4.5 | - 0.13 ± 0.61 |
| Avonmouth | 4.21 | 4 | 9.9 | - |
| Holyhead | 0.33 | 2 | 5.2 | - |
| Immingham | 4.03 | 3 | 5.7 | - |
| Heysham | 4.22 | 4 | 5.8 | - |
| Portpatrick | 8.33 | 8 | 9.0 | + 0.84 ± 1.12 |
| N Shields | 4.26 | 5 | 5.2 | - |
| Millport | 4.15 | 4 | 7.8 | - |
| Stornoway | 5.96 | 5 | 16.1 | - |
| Lerwick | 7.23 | 6 | 12.0 | - |

Table 4  EGPS Station Results Summary

The results given in Table 4 confirm that it has been possible to obtain a height standard deviation of about 5 to 10 mm when using episodic GPS data over the period from 1991 to 1999.  Table 4 also includes vertical station velocities, with corresponding standard errors, for the 4 EGPS stations with the longest time series.

Considering the trends in the vertical station velocities obtained for the 4 EGPS stations with the longest time series, there is a suggestion of subsidence at Portsmouth and Newhaven, uplift at Portpatrick and relatively little movement at Dover.  These are the first indications that the GPS estimates of current vertical land movements at these 4 tide gauge sites are consistent with the coarse spatial pattern of vertical land movements based on geological information (Shennan, 1989).

The height standard deviations obtained for the other 9 EGPS stations are consistent with those obtained for Portsmouth, Newhaven, Dover and Portpatrick and confirm that it will be possible to obtain an assessment of vertical land movements at these tide gauge sites with longer time series.

- Conclusions and Recommendations

The main implications of the findings of the research project are that:

- By establishing CGPS stations in the UK it has been possible to obtain vertical station velocities with time series of greater than 18 months, from which an initial assessment of current vertical land movement at the Sheerness tide gauge site has been made.

- By using episodic GPS data only, it has been possible to obtain vertical station velocities with height time series of 8 years, from which an initial assessment of current vertical land movements at the Portsmouth, Newhaven, Dover and Portpatrick tide gauge sites has been made.

- With the availability of CGPS stations in the UK, improved height estimates can be obtained for EGPS stations by using the new monitoring strategy.

The recommended action resulting from the research is to continue using the new monitoring strategy developed as part of this research project.  Where possible, CGPS stations should be established at tide gauge sites, particularly those located in critical coastal zones.  The other tide gauge sites should then be monitored using a ’roving GPS receiver’.  Following Dixon (1991), if the height time series are extended it should be possible to detect vertical land movements of 1 mm/yr, to a precision of ± 0.4 mm/yr, at any CGPS stations with 6 years of continuous GPS data and at any EGPS stations with 12 years of episodic GPS data.

In addition to continuing to use the new monitoring strategy, future research should concentrate on time series analysis to better understand the variations in height time series and the testing of the dual-CGPS station concept, in order to improve the reliability of any estimates of vertical land movements in the UK.

# ABSOLUTE GRAVITY MEASUREMENTS

1   Scientific objectives

The overall objective of the absolute gravity work is to formulate a procedure that can be used for measuring vertical land movements at UK tide gauges, in order to be able to separate the climate related changes in mean sea levels from the component due to land movements. This involved the establishment of new absolute gravity sites near selected tide gauges of the National Tide Gauge Network and re-measurement of gravity at those sites. In order to ensure that the POL absolute gravimeter (FG5-103) measures gravity with an accuracy equivalent to the highest international standards, an important part of the procedure is to inter-compare the POL absolute gravimeter with other absolute gravimeters, whenever the opportunity arises.

2   The absolute gravimeter

The FG5 absolute gravimeter is the latest in a series of technical developments made over many years by the USA National Institute of Standards and Technology and the University of Colorado (Niebauer et al., 1995). It is now produced commercially by Micro-g Solutions Inc., Colorado, USA. The principal of the absolute gravimeter is straightforward in that it measures the acceleration of a mass in free fall in a vacuum. However, in order to achieve an accuracy of 2 parts in a billion of gravity (i.e. 20 nm/sec² or 2 microgals) several technical advances have been made so that various possible sources of systematic errors are reduced to well below this level. The falling mass is a corner-cube retroreflector and its position is measured using a laser interferometer. The light path to the corner-cube forms one arm of the interferometer and a corner-cube mounted on an active long period seismometer (Super Spring), so as to act an inertial reference mass, forms the other arm of the interferometer. The interference fringes between the 2 light beams are counted and timed and the distance-time pairs collected during the 20cm drop are used in the equation of motion to solve for the acceleration due to gravity ‘g’. The whole system is automatically controlled by computer and typically 200 drops i.e. 200 independent determinations of ‘g’, are made per hour. The key to the accuracy of the FG5 absolute gravimeter is that the measurements are directly related to international standards of length and time. The instrument uses a newly developed iodine-stabilised laser, which is the international length standard. A rubidium frequency reference is used for timing and this can be calibrated against a caesium standard. For further details of the instrument and the technical developments see Niebauer et al. (1995).

3   Methodology

For this work it was decided to concentrate on 3 UK tide gauges, which are considered to be the core UK tide gauges. These are the tide gauges at Newlyn, Lerwick and Aberdeen. Newlyn and Lerwick are UK tide gauges which contribute to the fundamental network of global tide gauges, which form the Global Sea Level Observing System (GLOSS) coordinated by the Intergovernmental Oceanographic Commission. Newlyn is also important because of its long, high quality mean sea level time series and it is the tide gauge that defines the datum of the UK height reference system. Aberdeen is important because it has the longest UK tide gauge time series (137 years).

Since the absolute gravimeter produces typically 200 values of gravity per hour, it is common practice to measure gravity at a site by measuring for 1 day or even just for a few hours. The procedure developed for the present work was to measure for at least 3 days, with the gravimeter being carefully set-up again at the start of each day. This not only produced significantly more data for a given field trip, but also allows a comparison of the standard deviations of the hourly means each day with the variablity from day to day. This enables the assessment of the noise in the measurements at a particular site and epoch. Before and after each field visit, measurements were made at the gravity site in the sub-basement of Bidston Observatory (POL), in order to ensure that the absolute gravimeter gave consistent values. The long series of measurements at POL had already clearly shown that one of the main sources of noise in the absolute gravity measurements is due to microseisms, which typically have periods from 5 to 7 seconds. These are generated by ocean waves and are therefore important at coastal sites. The Super Spring has a period of about 60 seconds, in order to reduce the effects of high frequency noise. However, on very windy days the energy in the microseismic band increases significantly and oscillations of the reference mass give an increase in the noise of the gravity measurements. The extended visits to each site are therefore also valuable, since this allows the possibility of avoiding days with very high microseisms.

Before making any gravity measurements, a reconnaissance visit was made in order to choose the best available site. Buildings on solid bedrock were chosen, which is important for both stability and for being representative of the vertical crustal movements of the area. Nearby ‘witness’ gravity stations were set-up and measured relative to the absolute gravity station by the University of Edinburgh using LaCoste and Romberg relative spring gravimeters. Newlyn and Aberdeen are also part of the British Precise Gravity Network (BPGN), which consists of 65 gravity sites covering most of Britain, that have been measured by the University of Edinburgh using the relative spring gravimeters. Measurements with the POL absolute gravimeter at Wick, Aberdeen, Edinburgh, POL, Herstmonceux, Taunton and Newlyn have been used to fix the datum and scale of this relative network.

An important part of the methodology is to ensure that the absolute gravimeter continues to give results with an accuracy equivalent to the highest international standards. The POL absolute gravimeter has therefore been regularly inter-compared with other absolute gravimeters. Whenever the instrument is returned to the manufacturer, Micro-g Solutions USA, for service, the opportunity is taken to make measurements at the USA fundamental gravity site at Table Mountain in Colorado and to compare the results with measurements made with other FG5 gravimeters. Inter-comparison experiments have also been made with other absolute gravimeters at European sites in Germany, Belgium, Italy and France. The latter measurements were made at the Bureau International des Poids et Mesures (BIPM) near Paris during the inter-comparison experiment between all available absolute gravimeters, which is organised every 4 years. In these various inter-comparisons FG5-103 was verified to be in agreement with other FG5 absolute gravimeters at the 20 nm/sec² (2 microgals) level, which is the specified accuracy of the instrument.

4   Results

The new absolute gravity sites were established at Newlyn and Aberdeen and the first absolute gravity measurements taken in 1995. Absolute gravity measurements began in Lerwick in 1996. The absolute gravity results obtained at these sites are given in Tables 5, 6 and 7 respectively.

| Year | Day of Year | Gravity ((gals) | Stand. Dev.((gals) |
| --- | --- | --- | --- |
| 1995 1995 1995 1995 1995 1997 1997 1997 1997 1998 1998 1998 2000 2000 2000 | 282 283 284 285 286 174 175 176 177 180 181 182 031 032 033 | 981046524.3 981046524.9 981046524.5 981046527.3 981046527.2 981046525.3 981046524.7 981046526.3 981046527.4 981046529.6 981046521.5 981046524.1 981046524.7 981046525.6 981046524.5 | 1.9 1.1 2.4 1.4 1.3 1.0 1.9 1.6 1.8 3.7 0.8 0.8 1.6 1.9 1.8 |

# Table 5 Newlyn absolute gravity results

| Year | Day of Year | Gravity ((gals) | Stand. Dev.((gals) |
| --- | --- | --- | --- |
| 1995 1995 1995 1996 1996 1997 1997 1997 1997 1998 1998 1998 1998 1999 1999 1999 | 311 312 313 267 268 188 189 190 191 201 202 203 204 226 227 228 | 981688373.0 981688371.8 981688372.5 981688371.6 981688369.5 981688375.4 981688372.8 981688372.7 981688373.4 981688372.1 981688372.5 981688372.2 981688372.0 981688365.7 981688364.1 981688364.3 | 2.6 2.6 2.8 2.2 2.5 2.6 2.3 2.7 2.2 2.5 1.9 2.1 2.1 1.6 2.1 2.5 |

Table 6  Aberdeen absolute gravity results

| Year | Day of Year | Gravity ((gals) | Stand. Dev.((gals) |
| --- | --- | --- | --- |
| 1996 1996 1996 1996 1996 1998 1998 1998 1999 1999 1999 1999 | 273 274 275 276 277 208 209 210 230 231 232 234 | 981944011.5 981944007.7 981944004.8 981944006.0 981944008.2 981944008.8 981944009.4 981944009.1 981944010.3 981944011.1 981944009.4 981944009.0 | 3.1 2.1 1.5 2.4 4.6 0.9 0.7 0.7 1.7 2.0 1.2 0.8 |

Table 7  Lerwick absolute gravity results

The gravity values are the mean values over that day and the final column gives the standard deviation of the hourly means during that day. It can be seen that Newlyn and Lerwick are very quiet sites with the standard deviations often being less than 2 microgals and sometimes less than 1 microgal. In contrast, Aberdeen usually has a higher noise than the other 2 sites and also shows more variability from year to year. Figure 4 shows the absolute gravity time series for Newlyn and Lerwick .It can be seen that Newlyn is particularly stable and has an overall change of gravity of less than 1 microgal from 1995 to 2000. The Lerwick results show an overall increase of gravity of just over 2 microgals from 1996 to 1999. A height increase of the surface of the Earth by 1mm gives a decrease of gravity of 0.2 microgals. Fitting a least squares trend to the Newlyn data gives a vertical land movement of + 0.9mm/year ( 1.5 mm/year. The Lerwick data gives a vertical land movement of –4.0 (1.9 mm/year. The subsidence at Lerwick is just significant (at the 2( level), whereas the land movement at Newlyn is not yet statistically significant. The only suitable geophysical model to compare with these observations is a model for the post-glacial rebound component of land movements developed by Lambeck and Johnston (1995). This model predicts that Newlyn and Lerwick should currently have vertical land movements of -1mm/year and –2mm/year respectively. The predicted subsidence at these 2 sites is mainly due to the so called hydro-isostatic subsidence caused by the long term viscous response of the Earth’s mantle to the loading from the increased mass in the oceans following the melting of the major ice sheets at the end of the last ice age.

Figure 4  Absolute gravity observations at Newlyn and Lerwick

Overall, the absolute gravity results are very encouraging and show that the careful procedures that have been developed are giving very consistent results. Longer time series of absolute gravity observations will give reduced errors in the trend estimates and increase the significance of the measured land movements.

- Conclusions and Recommendations

It has been demonstrated using absolute gravity measurements spanning 3 to 4 years that this technique has now advanced to the stage where it can be used to measure vertical land movements at coastal sites. Within the error estimates, the land movements at Lerwick and Newlyn are in agreement with a model of large scale movements due to post-glacial subsidence.

It is recommended that longer time series of absolute gravity measurements should be collected, so that the errors in the vertical velocity estimates are reduced to a few tenths of a mm per year. A comparison of the land movements determined using absolute gravity with the corresponding land movements determined from GPS will allow an assessment of any remaining systematic errors in these new techniques.

REFERENCES

Ashkenazi, V, Beamson, G A, Bingley, R M, Dodson, A H and Baker, T F, 1994.  The Determination of Tide Gauge Heights Using GPS.  POL Internal Document No 75, August 1994.

Ashkenazi, V, Bingley, R M, Dodson, A H, Penna, N T, and Baker, T F, 1997.  The Determination of Tide Gauge Heights Using GPS (Second Report).  POL Internal Document No 125, August 1997.

Baker, T F, Curtis, D J, and Dodson, A H, 1995.  Ocean Tide Loading and GPS. GPS World, pp 54-59, March 1995.

Bingley, R M, Ashkenazi, V, Penna, N T, Booth, S J, Ellison, R A and Morigi, A N, 1999.  Monitoring Changes in Regional Ground Level, Using High Precision GPS.  Environment Agency R&D Technical Report W210, December 1999, ISBN 1-85705-121-1.

Boucher, C, Altamimi, Z, Feissel, M, and Sillard, P, 1996.  Results and Analysis of the ITRF94.  International Earth Rotation Service (IERS) Technical Note 20, Observatoire de Paris.

Boucher, C, Altamimi, Z, and Sillard, P, 1998.  Results and Analysis of the ITRF96.  International Earth Rotation Service (IERS) Technical Note 24, Observatoire de Paris.

Boucher, C, Altamimi, Z, and Sillard, P, 1999.  Results and Analysis of the ITRF97.  International Earth Rotation Service (IERS), Observatoire de Paris.

Carter, W.E., Aubrey, D.G., Baker, T.F., Boucher, C., Le Provost, C., Pugh, D.T., Peltier, W.R., Zumberge, M., Rapp, R.H., Schutz, R.E., Emery K.O. and Enfield, D.B., 1989.  Geodetic fixing of tide gauge bench marks. Woods Hole Oceanographic Institution Technical Report, WHOI-89-31, 44pp.

Carter, W.E. (Ed.). 1994. Report of Surrey Workshop of the IAPSO Tide Gauge Bench Mark Fixing Committee held 13-15 December 1993 at the Institute of Oceanographic Sciences Deacon Laboratory, Wormley, UK. NOAA Technical Report NOSOES0006. 81pp.

Dixon, T H, 1991.  An Introduction to the Global Positioning System and Some Geological Applications.  Reviews of Geophysics, Vol 29, No 2, pp 249-276.

Dodson, A H, Shardlow, P J, Hubbard, L C M, Elgered, G, and Jarlemark, P O J, 1996.  Wet Tropospheric Effects on Precise Relative GPS Height Determination.  Journal of Geodesy, Vol. 70, pp 188-202.

Lambeck, K. and Johnston, P., 1995.  Land subsidence and sea-level change: Contributions from the melting of the last great ice sheets and the isostatic adjustment of the Earth, in Land Subsidence, ( Eds. Barends, Brouwer and Schroder), 3-18. Balkema, Rotterdam. ISBN 90 5410 589 5

Le Provost, C, Genco, M L, Lyard, F, Vincent, P, and Canceil, P, 1994.  Spectroscopy of the World Ocean Tides from a Finite Element Hydrodynamic Model.  Journal of Geophysical Research, 99, C12, pp 24,777-24,797.

Neilan, R.E., Van Scoy, P.A. and Woodworth, P.L. (Eds). 1997.  IGS-PSMSL Workshop on methods for monitoring sea level: GPS and tide gauge benchmark monitoring and GPS altimeter calibration. Proceedings of meeting March 17-18, 1997, JPL, Pasadena, California, USA. JPL Publication 97-17 3/98, pp 202.

Niebauer, T.M., Sasegawa, G.S., Faller, J.E., Hilt, R. and Klopping, F., 1995.  A new generation of absolute gravimeters. Metrologia, Vol. 32, 159-180.

McCarthy, D D (Editor), 1992.  IERS Standards (1992).  International Earth Rotation Service (IERS) Technical Note 13, Observatoire de Paris, July 1992.

Niell, A E, 1996.  Global Mapping Functions for the Atmospheric Delay at Radio Wavelengths.  Journal of Geophysical Research, Vol 101, No B2, pp 3227-3246.

Rothacher, M, Schaer, S, Mervart, T L, and Beutler, G, 1995.  Determination of Antenna Phase Centre Variations Using GPS Data.  Proceedings of the 1995 IGS Workshop, Potsdam, May 1995.

Saastamoinen, S, 1973.  Contributions to the Theory of Atmospheric Refraction.  Bulletin Geodesique, in three parts; 105 pp 279-298, 106 pp 383-397, 107 pp 13-34.

Shennan, I, 1989..  Holocene Crustal Movements and Sea Level Changes in Great Britain.  Journal of Quaternary Science, 4, pp 77-89.

Stewart, M P, Ffoulkes-Jones, G H, Chen, W, Ochieng, W Y, Shardlow, P J, and Penna N T, 1997.  GPS Analysis Software (GAS) Version 2.4 User Manual.  IESSG Publication, University of Nottingham.

Woodworth, P L, 1999.  A Study of Changes in High Water Levels and Tides at Liverpool During the Last Two Hundred and Thirty Years with some Historical Background.  Proudman Oceanographic Laboratory Report, No 56.

Woodworth, P L, Tsimplis, M N, Flather, R A and Shennan, I, 1999.  A Review of the Trends Observed in British Isles Mean Sea Level Data Measured by Tide Gauges.  Geophysical Journal International, 136, pp 651-670.

Please press enter

# Text boxes

- To move from one fill-in location (field) to another, press TAB, RETURN, UP or DOWN arrow keys unless instructed to do otherwise. Locations may also be selected by clicking on them.