ministry of agriculture, fisheries and food	CSG 15

Research and Development

Final Project Report

(Not to be used for LINK projects)

Two hard copies of this form should be returned to: Research Policy and International Division, Final Reports Unit MAFF, Area 6/01 1A Page Street, London SW1P 4PQ An electronic version should be e-mailed to c.csgfinrep@csg.maff.gsi.gov.uk

| Project title | Extension of National Appraisal of Assets at Risk from Flooding and Coastal Erossion |
| --- | --- |

| MAFF project code | FD2004 |  |
| --- | --- | --- |

| Contractor organisation and location | Halcrow Group Ltd, Burderop Park, Swindon, Wiltshire, SN7 0QD |
| --- | --- |

| Total MAFF project costs | £ 105,106 |  |
| --- | --- | --- |

| Project start date | 23/10/00 |  | Project end date | 28/11/01 |
| --- | --- | --- | --- | --- |

Executive summary (maximum 2 sides A4) To tab in this section press the tab key and the Control key together Press the DOWN arrow once to move to the next question.

This research has further developed preceding work to evaluate the national economic impacts of flooding and coastal erosion (carried out under the MAFF research project FD1702, published in 2000). The overall aim of the research is unchanged form that previous study. It has sought to quantify the economic benefits afforded nationally through the provision of flood and coastal defences and to evaluate this against the required budgets necessary to maintain and improve these defences.

The resulting analysis has enable the expression of damages and damages avoided in terms of a national benefit / cost summary which accounts for the assessment of economic damages under three scenarios:

“do nothing”,

maintain current standards of defence

and, improve defences to an indicative standard.

The results of the research have been used by DEFRA to provide support to the spending review process, helping to inform decisions taken regarding future budgetary provisions for the funding of capital works and defence maintenance. Following the completion of the research, the results have also been presented region by region within the Environment Agency (EA) via a series of workshops aimed at trying to build up a more definitive medium and long term works programme for the construction and maintenance of defences.

Areas where research has moved forward from the preceding published work have been:

to extend the area of the study into the Welsh EA Region,

to refine the evaluation of damages caused to agriculture,

to examine the disrupting effects of flooding on road traffic,

and to estimate the potential impacts of climate change on damages.

The conclusions from this research project are as follows:

- Approximately 10% of the population of England and Wales live within areas potentially at risk from flooding or coastal erosion, whilst approximately 12% of the agricultural land (including 61% of the country’s Grade 1 agricultural land) is also located in these areas;

- Property worth over  £220 billion and agricultural land worth approximately £7 billion is located within these areas potentially at risk;

- Without any flood and coastal defences, the annual average economic damage (AAD) from flooding and coastal erosion in these areas would be over £3.5 billion/year;

- The capital works and maintenance investment needed to continue to provide and maintain present defence standards is in excess of £0.3 billion/year;

- Current standards of defence reduce annual average damages to approximately £0.8 billion/year;

- Continuing to invest at present levels of approximately £0.24 billion per year will result in increasing annual average damage possibly at the rate of some £10-15 million per year.

- Accommodating climate change is likely to require a further increase in investment of between 10% and 20% over and above that required to meet indicative standards under present day conditions;

- Without allowance for accommodating the predicted impacts of climate change within defence provision the economic impacts associated with flooding could increase significantly, with annual average damages increasing in fluvial areas by approximately 50% and in excess of 200% on the coast by the year 2050.

The current study has involved some broad-based assumptions and there is scope to further improve upon the accuracy of the analysis. However, there is sufficient confidence in the order of magnitude of the results to conclude that there is a need to reappraise even the recently enhanced levels of funding for flood and coastal defence.

Although definitive arguments regarding how and where to invest should not be drawn from this study, there is little doubt that there is a clear need to substantially increase expenditure on flood and coastal defence to maintain the same level of protection as that which currently exists. Failure to do so will inevitably lead to an increase in economic damages year by year, i.e. when another significant event occurs, such as in 1953 or 2000, the extent of area affected and the resulting losses/damage could potentially be significantly greater unless the rate of investment in replacement or renewal of defences is increased. It should also be noted that present defences appear, in several places, to be below the indicative standards recommended in FCDPAG3.

The earlier study (2000) indicated that present investment levels needed to be increased by between 50% and 100%, based upon an investment of approximately £0.2billion/year. This is modified to 25% to 65% based upon the current revised investment of £0.24 billion/year. The conclusions from assessing climate change impacts are that a 35% to 85% overall increase may however still be required to meet indicative standards of protection over the next 50 years.  Although the most severe impacts of climate change may not be experienced for some time, it is apparent that it is likely to be well worthwhile to make advance investments to accommodate climate change.  The balance between gradually providing higher standards as defences require replacement and making provision for future improvements needs to be considered on a case by case basis but where significant works are deferred then the adaptation costs will be additional to those of the normal replacement cycle.

If investment is maintained at or around present levels, the results imply that effective protection can only be provided to selected areas of the country, i.e. a conscious decision might be required to abandon defences to some less populous areas. This leads to further questions, such as “where new residential properties and businesses should be located?”. This study cannot attempt to resolve such issues, though the mapping out of the value of assets, calculated damages and indicative and current standards of protection can at least provide a preliminary focus in the consideration of where priorities for defence provision should lie.

Scientific report (maximum 20 sides A4) To tab in this section press the tab key and the Control key together Press the DOWN arrow once to move to the next question.

# INTRODUCTION

Research commissioned by MAFF in 1999 – 2000, under the National Appraisal of Assets at Risk from Flooding and Coastal Erosion project, set out with following objectives:

- gather information on the extent of the areas at risk and the assets in those areas,

- update and improve the 1997 Comprehensive Spending Review (CSR) valuation of the risks,

- consider a range of scenarios for future investment, and

- to recommend potential future improvements to the analysis.

The summary results it produced were that:

- the value of the assets at risk is approximately £214 Billion,

- the potential annual average damages (without defences) are about  £2.8 Billion,

- the current annual average damages are about  £600 Million, and

- the current capital expenditure on asset renewals could be about half that required to maintain current standards.

(Burgess K A, et al 2000)

Recommendations for further research made at the conclusion of that first phase of study were that:

- the research be extended into the area covered by the Welsh Region of the Environment Agency, so as to provide full national coverage of the research within England and Wales,

- additional research be undertaken within the English EA regions to try to improve our knowledge of current flood defence standards,

- the effects of climate change on flood frequency and economic damages be incorporated into tidal and fluvial flood scenarios,

- methodologies formulated for examining the economic impacts of flooding on agricultural production and road traffic disruption be put into practice to enable additional components of economic damages to be brought into the national benefit / cost assessment.

From a technical standpoint the key differences between this and the preceding research are in the approaches and results generated through the development of the climate change analysis, and in the further development of agriculture and traffic disruption damage calculations. The following sections outline the approaches developed to address these new aspects of research. They are fully documented in the Technical Report that has been issued to accompany the study’s Final Report.

# CLIMATE CHANGE SCENARIOS

The main basis for establishing the potential impacts of predicted future climate change on flood frequency and flood damage has been to assume deterioration in current standards of service relative to increases in peak river flow, tidal water levels and predicted changes in wave characteristics. Combined with these effective reductions in standard of service (SOS), work has also been undertaken to re-evaluate increases in typical flood damage cost estimates associated with given return period events.

## Establishing the future climate

Of key influence to the study findings has been the choice of climate change scenario and Genral Circulation Model (GCM) used to predict the associated changes in the fluvial and tidal environments. There are a large number of different GCM’s and also Regional Climate Models. The main purpose of developing and using such models has been to investigate the effects of global warming by introducing increased ‘greenhouse gas’ concentrations.

The Intergovernmental Panel on Climate Change (IPCC) established a Task Group on scenarios for Climate Impact Assessments. This group established criteria to identify GCM experiments whose results could be deposited at the IPCC Data Distribution Centre (DDC).

The UK Hadley Centre for Climate Predictions and Research (HADCM2) and the MAX Planck Institute for Meteorology (Hamburg) (ECHAM4) are two modelling centres that meet the IPCC requirements and are commonly used in climate change studies carried out in Europe. The use of results from both of these models was considered within this project.

## The Tidal Scenario

For the purposes of this study the ECHAM4 model was chosen to simulate climate change within the tidal environment as it has been shown to simulate higher wind speeds well in coastal locations.  In addition, HR Wallingford is currently working on another MAFF funded project ‘Coastal Defence Vulnerability 2075’ that uses data from the ECHAM4 Global Climate Model and maintaining consistency in approach between the two studies was an important consideration.

The data provided by the Coastal Defence Vulnerability 2075 project consists of two, 30-year time blocks: one representing the present day, one representing the future.  The data consist of wind speeds and water levels at 6-hourly intervals and is available for five different locations around the UK: offshore of Mablethorpe, Dungeness, Lyme Bay, Swansea Bay and Blackpool.

The thirty-year time series’ of wind data were  transformed to wave data and have then been combined with the water level data before running through HR’s JOIN-SEA software.  JOIN-SEA is joint probability software that uses a monte-carlo simulation technique to generate many (10,000) years worth of wave and water level data, on which extremes analyses can be carried out.

In summary, 10,000 years worth of wave and water level data have been generated based on present day conditions and 10,000 years worth of data based on future conditions, at each of the five locations around the UK.

## The Fluvial Scenario

GCMs operate at spatial and temporal scales which are greater than the extent of any UK catchment or the typical duration of a flood. In addition the GCM simulations differ according to the exact model being used such as the HADCM2 or the ECHAM4 models of the Hadley Centre and the Max Plank Institute respectively.

In order to generate future scenarios of flood discharge directly, a methodology is needed to generate point rainfall and other appropriate meteorological time series for future climate scenarios based upon historic records at the site and scenario predictions from a GCM. There are several approaches possible including:

- generation of precipitation series from historic series but adjusted to match broad scenario statistics from the GCM

- the use of stochastic weather generators based upon the broad data from GCM scenarios

- statistical Expanded Downscaling (EDS) to produce future scenarios at particular weather stations, see Bürger (2000),

- the use of regional climate models (RCMs) at a substantially finer scale than the GCM

There have been many research studies over the past decade covering the potential impacts of climate change on river flood frequency in the UK see for example Naden et al (1996) and Calver et al (1999).

In determining the impacts of climate change upon flood extent and thus risk, key parts of the process are:

- the change in precipitation – by annual amount, seasonally, number of storms, intensity of rainfall etc

- the response of parts of the hydrological cycle to climate changes – vegetation, evapotranspiration, soil moisture

- the response of the river and flood plain system

- the vulnerability of land use and occupation to flood damage (and trends in these).

All of these factors contain considerable uncertainty and currently, there is no scientific consensus on the best resolution of all the technical issues in assessing the impact of climate change on the frequency of the extent of flooding.  The EUROTAS project (Samuels, 2001) demonstrated the feasibility of continuous simulation hydrological modelling coupled to river modelling using a GIS framework with down-scaled GCM information at the catchment scale.  However, within the context of the current project it was not appropriate to embark upon a simulation exercise of all UK catchments, or even a selection of catchments in each geographical region and an alternative approach was devised.

Rather than tying the economic assessments to specific climate simulations from a particular GCM and emission scenario, the sensitivity of the national economic assessment of flood damages was based upon broad scenarios of increases in regional flood discharge.  These are expressed as percentage change from the “current” condition, without reference to a specific GCM, emission scenario or decade of assessment.

The regional information across the UK is taken from the Flood Studies Report (FSR) (NERC, 1975) and the supplementary report series.  The information in the Flood Estimation Handbook (CEH, 2000), whilst being more recent is based upon flood frequency in specific catchments rather than in broad geographical regions.  A particular advantage of the FSR is that the regional information is still closely aligned with the Environment Agency regional boundaries, which form the basis of the regional assessment in the current economic appraisal.

The following assumptions are made

- that flood peak discharge is an appropriate measure of the hazard

- that peak flood discharge increases proportionately for all return periods (that is the shape of the regional growth curve is unaffected by climate change)

- that there are no large-scale river changes which affect the stage-discharge relationship at the catchment scale

- that the performance of flood defence infrastructure, and hence damage, is related to the value of peak discharge

The information used in the flood damage assessments relates flood damage to the current return period of the flood.  Thus to simplify the use of the tabulated of damages, the future frequency of current flood return periods was assessed, for example, by determining the future return period of the current 100 year flow in the Anglian region.  A methodology was developed to provide a future return period for any current return period in any FSR region, for percentage changes in flood flow from –10% to + 25%.

Results for Annual Average Damage (AAD) to built property within the fluvial floodplain were calculated under 10% and 20% increases in flood flow. This has allowed a comparison of the sensitivity to increases in flows to AAD in each of the EA Regions.

# CHANGES TO STANDARDS OF SERVICE

## Coastal response function and standard of service

For the purposes of this project the SOS has been directly related to the change in the return period of specified overtopping rates. This rate has been chosen as the coastal response variable most appropriate to characterise SOS, as it is closely linked to breach probability, is relatively well understood and is influenced by both water levels and wave conditions.

Overtopping performance however, is dependent on structure type.  Therefore, three ‘typical’ structure types have been identified that can be readily incorporated at a national scale using the existing EA data.  These types are:

- Vertical sea walls

- Embankments

- Shingle beaches

Overtopping rates have been calculated for the three structure types using well-established empirical methods developed by HR and described in EA (1999).  These empirical methods require wave conditions at the toe of the structure to be specified. The formulae are based on the maximum wave height ‘allowable’ in a specified water depth.  The wave height is then calculated as a function of water depth. This simplified approach has been adopted for use in this study, where many thousands of wave transformation calculations are required.

Use of the simplified approach requires the water depth at the structure toe to be specified.  This decision is critical when assessing the coastal defence response to future climate.

A consistent, but arbitrary, method has been devised for specifying the toe and crest levels for the three different structure types. ‘Typical’ structure type/ toe level combinations have been considered when defining these levels, however, it is acknowledged that many and wide variations on the specified ‘typical’ structures will exist around the coast of the UK. This kind of broad assumption is necessary and consistent with the methodology adopted in other aspects of this project.

Tables 3.1 to 3.3 describe the calculated reductions in Current Standard of Service for the three typical structure types defined within the study.

| Vertical Wall | 2075 Standard |
| --- | --- |
| Present Standard | East Coast | South East Coast | South West Coast | Bristol Channel | North West |
| 2 | <2 | <2 | <2 | <2 | <2 |
| 5 | <2 | <2 | <2 | <2 | <2 |
| 10 | 2 | <2 | <2 | <2 | 2 |
| 20 | 3 | <2 | 5 | <2 | 3 |
| 50 | 10 | 2 | 15 | 2 | 10 |
| 100 | 15 | 4 | 40 | 3 | 20 |
| 200 | 40 | 10 | 100 | 10 | 30 |

Table 3.1 Reduced SOS for vertical walls

| Embankment | 2075 Standard |
| --- | --- |
| Present Standard | East Coast | South East Coast | South West Coast | Bristol Channel | North West |
| 2 | <2 | <2 | <2 | <2 | <2 |
| 5 | 2 | <2 | <2 | <2 | <2 |
| 10 | 3 | <2 | <2 | 2 | 2 |
| 20 | 5 | <2 | 3 | 3 | 3 |
| 50 | 10 | 2 | 15 | 5 | 10 |
| 100 | 25 | 3 | 40 | 10 | 20 |
| 200 | 70 | 5 | 80 | 15 | 60 |

Table 3.2 Reduced SOS for embankments

| Shingle Beach | 2075 Standard |
| --- | --- |
| Present Standard | East Coast | South East Coast | South West Coast | Bristol Channel | North West |
| 2 | <2 | <2 | <2 | <2 | <2 |
| 5 | 2 | <2 | <2 | <2 | <2 |
| 10 | 3 | <2 | <2 | 2 | 2 |
| 20 | 5 | <2 | 3 | 3 | 3 |
| 50 | 10 | 2 | 15 | 5 | 10 |
| 100 | 30 | 3 | 40 | 15 | 20 |
| 200 | 80 | 5 | 80 | 20 | 50 |

Table 3.3 Reduced SOS for shingle beaches

Regional Changes to Fluvial Standards of Service

The future return period associated with the current 100-year flood for a uniform 20% increase in peak discharge is shown in Figure 3.1. Considerable regional variation is evident with the influence being least in Anglian region and greatest in Ireland.

These results were used in each region with 10% and 20% flood discharge increase scenarios. The figure of 20% is broadly in line with the scenarios of increase in winter precipitation by the 2080’s for the current UKCIP studies (Hulme & Jenkins, 1998) and appears as an illustrative assessment scenario in the new PPG 25 on development and flood risk (DETR, 2001).  The study reported by Naden et al (1996) indicated increases of about 10% for the Rivers Severn, Thames and Trent for the 50-year flood by the 2050’s, based upon one of the earlier 1992 Hadley Centre GCM scenarios.

Figure 3.1 Illustration of the effect of climate change on river flow

Interpreting these flood flow increases in terms of regional reductions in SOS the following results have been obtained:

|  | Reduced SOS |
| --- | --- |
| Current SOS | Anglian | Midlands | North East | North West | Southern & Thames | South West | Wales |
| 5 | 3.9 | 3.5 | 3.3 | 3.2 | 3.8 | 3.4 | 3.4 |
| 10 | 7.6 | 6.8 | 6.3 | 6.2 | 7.4 | 6.7 | 6.5 |
| 25 | 18 | 17 | 15 | 15 | 18 | 16 | 15 |
| 50 | 36 | 33 | 29 | 29 | 35 | 32 | 30 |
| 100 | 70 | 65 | 56 | 57 | 68 | 64 | 58 |
| 200 | 137 | 130 | 109 | 113 | 133 | 126 | 114 |

Table 3.4 Region reduction in SOS under 10% fluvial flood flow increase

|  | Reduced SOS |
| --- | --- |
| Current SOS | Anglian | Midlands | North East | North West | Southern & Thames | South West | Wales |
| 5 | 3.2 | 2.6 | 2.5 | 2.3 | 3.1 | 2.6 | 2.5 |
| 10 | 5.9 | 4.9 | 4.3 | 4.2 | 5.7 | 4.8 | 4.5 |
| 25 | 14 | 12 | 9.6 | 9.6 | 13 | 11 | 10 |
| 50 | 26 | 23 | 18 | 18 | 25 | 22 | 19 |
| 100 | 50 | 44 | 33 | 35 | 48 | 43 | 36 |
| 200 | 96 | 87 | 63 | 68 | 91.65 | 83 | 69 |

Table 3.5 Region reduction in SOS under 20% fluvial flood flow increase

# BUILT PROPERTY DAMAGE INCREASE

By applying the reduced standards of service outlined in tables 3.1 to 3.5 to the asset database built-up during the previous phase of the study it was possible re-calculate the Annual Average Damages. The results provide an estimation of AAD for tidal flooding under the 2075 climate change scenario, and for fluvial flooding under 10% and 20% flood flow increases.

The AAD values calculated assume that defence structures remain physically unchanged e.g. where crest levels are currently sufficient to defend against a 2% (1 in 50 years) event now, that same crest height may in 2075 only represent adequate defence against a 4% (1 in 25 year) event. Tables 4.1 and 4.2 show the comparison of AAD values. It should be emphasised that in practice it is likely to be well worthwhile to mitigate against such increases in damage through additional defence works or other flood management activities. This practice is already recommended in DEFRA guidance and these figures amply illustrate the potential benefits of adopting such a precautionary approach.

| Region | 2001 AAD | 2075 AAD | % of current AAD |
| --- | --- | --- | --- |
| Anglian | £21.49 | £71.41 | 332 |
| Midlands | £4.54 | £34.87 | 768 |
| North East | £60.64 | £252.23 | 416 |
| North West | £18.78 | £76.24 | 405 |
| Lower Thames* | £36.94 | £163.67 | 443 |
| Southern | £43.79 | £285.00 | 651 |
| South West | £10.30 | £59.50 | 577 |
| Wales | £13.95 | £62.21 | 446 |
| Total | £210.43 | £1,005.13 | 478 |

Table 4.1 Calculated increases in tidal flood damage to built property due to climate change (£ millions) * N.B. no increase in AAD from flooding in the Tidal Thames upstream of the Barrier is assumed due to the assessed 0.1% defence standard in this reach.

|  | Current AAD | Predicted AAD | % of current AAD |
| --- | --- | --- | --- |
| Region | (£ million) | 10% Flood Flow Increase | 20% Flood Flow Increase | 10% flood flow increase | 20% flood flow increase |
| Anglian | £55.02 | £78.16 | £111.70 | 142 | 203 |
| Midlands | £54.85 | £85.71 | £129.06 | 156 | 235 |
| North East | £47.29 | £90.81 | £111.70 | 192 | 236 |
| North West | £19.22 | £34.03 | £54.45 | 177 | 283 |
| Thames | £201.26 | £245.21 | £295.45 | 122 | 147 |
| Southern | £15.51 | £22.28 | £32.69 | 144 | 211 |
| South West | £28.90 | £41.92 | £60.86 | 145 | 211 |
| Wales | 30.15 | 47.06 | 72.46 | 156 | 240 |
| Total | £452.20 | £645.18 | £868.37 | 143 | 192 |

Table 4.2 Calculated increases in fluvial flood damage to built property due to climate change (£ millions)

It should be noted that whilst these increases in damage appear exceptionally high, they are based on a 75 year time. To make a comparison with a 50 year time horizon, the %AAD increases will be closer to half to two-thirds of these values, i.e. the total in Table 4.1 may be 300-350% of current AAD (rather than 477%) and the totals in Table 4.2 closer to 120-130% (for the 10% flow increase), and 145-165% (for the 20% flow increase).

# FOREGONE AGRICULTURAL PRODUCTION

Separate to the work on damages to built property the study has also examined the potential economic impacts caused by flooding through foregone opportunities to agriculture. The approach taken was to establish a model of deterioration in the gross margin of production. This decline in gross margin is associated with a change in the agricultural production system from one of high to lower yields brought about through the abandonment of drainage and flood defence maintenance. Four basic management systems have been modelled, and these are detailed in table 5.1.

| Unimproved/ rough permanent pasture | Improved pasture | Arable system | Root System | Land use as reflected by current SoS |
| --- | --- | --- | --- | --- |
| n/a | n/a | n/a | n/a | Improved System |
| Beef system | Dairy | Arable | Roots | Current system |
| Reduced stocking | Reduced stocking | Lower yield arable | Arable | Intermediate deterioration |
| Rough grazing of store cattle | Rough grazing of store cattle | Rough grazing of Store cattle | Lower yield arable | Deterioration complete |

Table 5.1 Decline path for 4 main land management systems associated with a “Do Nothing” management policy.

The model effectively represents the losses accrued through a “Do Nothing” management scenario, and the losses have been calculated as Mean Annual Average Damages incurred over a 10 and 20 year period of decline in land management systems. The model has been applied to both coastal and fluvial floodplains.

Typical Land Management Systems and Gross Margins for the selected scenarios

In discussion with agricultural economists, the following land management scenarios have been deduced as representative of English/Welsh agriculture with respect to existing and deteriorating standards of service. It is fairly assumed that the existing land use within flood plains, as ascertained from the York/Cardiff MAFF June 4th agricultural statistics reflects the SOS currently provided. Any deterioration of this SOS will result in commensurate changes in land management systems. Table 5.2 summarises the adjusted gross margins for each land management system. Adjusted gross margins (i.e. gross margins adjusted by the appropriate factors to be applied to gross output to allow for domestic support costs) are calculated in line with the FCDPAG3 Scenario 3 – Partial loss of agricultural output.

However, for simplicity the gross margins are not converted to net margins by deducting changes in fixed costs at farm level through changes in the land management system. The fixed costs structures of farms are assumed not to be affected, though this would certainly not be the case in particularly large fenland farms, where cereal production deteriorates to extensive pasture. It is difficult to isolate differential fixed costs at this level of generality, and using Nix whole farm fixed costs and applying these to the changed management systems assumed distorts the analysis. In any case, as domestic subsidy has been subtracted from the gross output to simulate economic gross margins as against farm gate prices, fixed costs would have to be adjusted to give their equivalent economic values.

| Unimproved/ rough permanent pasture | Improved pasture | Arable system | Root System | Land use as reflected by current SoS |
| --- | --- | --- | --- | --- |
| As current | As current | As current | As current | Improved System |
| Single lowland sucklers (£210) | Dairy (£876) or 18 month beef (£338) (1a) | Arable rotation (2) (£448) Fens (£725) | Potatoes (£1,833) (3) | Current system |
| Single lowland sucklers (£135) | Dairy (£786) or 18 month beef (£172) (1b) | Arable rotation (£282) Fens (£348) | Arable rotation (2) (£448) Fens (£725) | Intermediate deterioration |
| Beef Stores summer finishing (£60) | Beef Stores summer finishing (£60) | Beef Stores summer finishing (£60) | Arable rotation (£282) Fens (£348) | Deterioration complete |

Notes: 	(1a)  Mean value £607;  (1b) Mean value £479. (2)  Arable default is 4 years Winter Wheat (£ 446); 1 Winter Oilseed Rape (£456). If East Anglia 4 years WW (£446); 1 Spring barley (£361); 1 potatoes (£,2205)

(3)   Mean of average and high yields

Table 5.2 Land use management systems and gross margins (£/hectare) (Nix 1999)

## Resultant Loses

Using production statistic from MAFF’s 1999 agricultural census it was possible combine current production values, gross margins and SOS values within the study GIS database. Using this information to calculate declining productivity over 10 and 20 year periods of decline the following economic losses have been calculated as Mean AAD values.

|  | Foregone Agricultural Production |
| --- | --- |
| Region | 10 year decay | 20 year decay | Built Property AAD |
| Anglian | £247.7 | £215.4 | £364.6 |
| Midlands | £67.9 | £59.2 | £367.7 |
| North East | £82.7 | £72.3 | £484.3 |
| North West | £29.6 | £26.1 | £195.5 |
| South West | £32.4 | £28.5 | £152.1 |
| Southern | £31.6 | £27.6 | £288.9 |
| Thames | £18.7 | £16.7 | £914.7 |
| Welsh | Not available | £42.5 | £178.7 |

Table 5.3 Foregone agricultural production as Mean AAD value (£ million).

# TRAFFIC DISRUPTION

Traffic disruption has been evaluated using techniques recommended in the Middlesex University FHRC Red Manual and updated using data and formulae as detailed in the Department of Transport/DoE COBA Manual Highways Economic Note 2, published in September 1996.

This method considers that travellers are consumers who derive benefits from arriving at their destination. Losses due to the flooding of road networks can therefore arise in two ways:

- The additional (i.e. marginal) transport costs of diverting around the flood by a slower, congested and/or more circuitous route; referred to as Vehicle Operating Costs (VOC)

- Opportunity costs to delayed travellers measured by putting an economic value on their working or leisure time; referred to as Value of Time (VoT)

The resource costs for traffic disruption during flood events are the difference between VOC and VoT during the flood event and during flood free conditions. Typical values for these costs have been calculated per km, and the length of A-road and motorways within each flood reach calculated. The value of annual average disruption costs (damages) have then been calculated as a function of the probability of flooding occurring in any one year, as per the calculations for built property damage.

Table 6.1 summarises the resource costs due to flood diversion for every kilometre of flood plain road affected. It is assumed that where a road crosses an indicative flood plain then, applying the assumed flood duration values in 6.1 will convert the average daily resource costs into event costs as per Table 6.2.

This model will be complex for the Fenland type situations or during widespread flooding, as diversions will not be possible without huge detours. Many of diverted routes will ‘cascade’ out of action as flooding becomes regional. The disruption figures represent a minimum economic cost of diversion, relating to the separate flooding of individual indicative flood plain compartments in partial isolation from other compartments.

| Road Type | VoT (£/day/km) | VOC (£/day/km) | Total resource costs (£/day/km) 1994 values | Total resource costs (£/day/km) (June 2000) |
| --- | --- | --- | --- | --- |
| Non Built up A roads Wales | 4,725 | 633 | 5,358 | 6,376 |
| Built up A roads Wales | 6,694 | 799 | 7,493 | 8,817 |
| Non Built up A roads England | 7,873 | 1,091 | 8,964 | 10,667 |
| Built up A roads England | 9,902 | 1,223 | 11,125 | 13,239 |
| Motorways Wales | 29,184 | 4,000 | 33,184 | 39,489 |
| Motorways England | 38,078 | 4,895 | 42,973 | 51,139 |

Table 6.1  Resource costs due to flood diversion

| Road Type | Total resource costs (£/day/km) (June 2000) | Flood Duration (hours) | Return period (years) | Event disruption costs (£) |
| --- | --- | --- | --- | --- |
| Non Built up A roads Wales | 6,376 | 6 | 5 | 1,594 |
|  |  | 12 | 10 | 3,188 |
|  |  | 24 | 50 | 6,376 |
|  |  | 48 | 100 | 12,752 |
|  |  | 96 | 200 | 25,504 |
| Built up A roads Wales | 8,817 | 6 | 5 | 2,204 |
|  |  | 12 | 10 | 4409 |
|  |  | 24 | 50 | 8,817 |
|  |  | 48 | 100 | 17,634 |
|  |  | 96 | 200 | 35,268 |
| Non Built up A roads England | 10,667 | 6 | 5 | 2,667 |
|  |  | 12 | 10 | 5,334 |
|  |  | 24 | 50 | 10,667 |
|  |  | 48 | 100 | 21,334 |
|  |  | 96 | 200 | 42,668 |
| Built up A roads England | 13,239 | 6 | 5 | 3,310 |
|  |  | 12 | 10 | 6,620 |
|  |  | 24 | 50 | 13,239 |
|  |  | 48 | 100 | 26,478 |
|  |  | 96 | 200 | 52,956 |
| Motorways Wales | 39,489 | 6 | 5 | 0 |
|  |  | 12 | 10 | 0 |
|  |  | 24 | 50 | 39489 |
|  |  | 48 | 100 | 78,978 |
|  |  | 96 | 200 | 157,956 |
| Motorways England | 51,139 | 6 | 5 | 0 |
|  |  | 12 | 10 | 0 |
|  |  | 24 | 50 | 51,139 |
|  |  | 48 | 100 | 102,278 |
|  |  | 96 | 200 | 204,556 |

Table 6.2 Average daily resource costs by road type and flood event (It is assumed that no motorways flood until the 50 year return period event.)

Table 6.3 presents the estimated AAD’s (£ million) attributable to traffic disruption under the three considered management scenarios. In all three the impacts represent less than 0.25% of the total national AAD’s attributable to the combined damages to built property, agriculture and traffic disruption.

|  | Tidal AAD | (£ million) |  | Fluvial AAD | (£ million) |  |
| --- | --- | --- | --- | --- | --- | --- |
|  | Do Nothing | Maintain Current | Maintain Target | Do Nothing | Maintain Current | Maintain Target |
| Anglian | 0.238 | 0.081 | 0.048 | 0.677 | 0.315 | 0.245 |
| Midland | 0.200 | 0.079 | 0.020 | 0.695 | 0.307 | 0.241 |
| North East | 0.237 | 0.121 | 0.099 | 0.356 | 0.177 | 0.143 |
| North West | 0.166 | 0.063 | 0.024 | 0.149 | 0.090 | 0.061 |
| South West | 0.052 | 0.017 | 0.006 | 0.213 | 0.135 | 0.070 |
| Southern | 0.243 | 0.076 | 0.016 | 0.129 | 0.062 | 0.049 |
| Thames | 0.302 | 0.073 | 0.018 | 0.500 | 0.333 | 0.170 |
| Wales | 0.087 | 0.023 | 0.010 | 0.173 | 0.104 | 0.079 |
| Totals | 1.526 | 0.533 | 0.241 | 2.894 | 1.525 | 1.058 |

Table 6.3 Annual Average Damages due to Road Traffic Disruption

# Recommendations

## Existing Improvements

Since the original study, completed in 2000, a number of actions have been taken. These include the joint DEFRA/Environment Agency development of the R&D Themes that are targeting future needs based upon industry requirements. This should include consideration of the findings of that previous study and new research to help address some of the limitations identified therein to provide improved accuracy in future analyses.

In addition, the Environment Agency, with DEFRA support, are now developing the National Flood and Coastal Defence Database (NFCDD), which will eventually provide the basis for regular assessments such as this through routine updating of the relevant datasets and the ability to resolve some of the analyses at a range of scales (i.e. local through to national).

Funding has also been made available for increased investment in capital works since the original study was completed. The annual budget of £150 million of capital works supported by DEFRA grant represents a 25% increase over the £110-120 million average in recent years.

Notwithstanding these improvements there will continue to be room for further advances in the work presented here. Full recommendations were made in the original report of 2000. These are summarised from that report in the following final sub-sections.

## Data and Analysis to Reduce Uncertainty

This study has established an analytical framework and combined data-sets for assessing national risks and investment needs. However, it has also drawn attention to the need for improved data to provide improved accuracy and confidence in the results and, in particular, to reduce dependence on some of the assumptions that have been required.

## Strategic Framework for Decision Making

The collection of new data and more efficient management of both new and existing information will enable the results to be improved and provide greater confidence in the recommendations as well as providing greater flexibility in their use. Given the conclusions of this study, and the possibility that investment to maintain or improve current defence standards throughout will not be forthcoming, there is a very real need to ensure that the strategic framework of national guidance will obtain the best value from available funds. The work already undertaken for this study forms the basic building block for development of such tools.

## Programme for Implementation

Accuracy of analysis and the ability to analyse strategic options will improve with time as more data becomes available. However, to maximise return on the present study and minimise uncertainty in future decision making, it is proposed that the recommendations made here are progressed henceforth.

The importance of good data cannot be over-stressed and future data collection needs to be integrated with the strategic assessment needs. A clear target for the Environment Agency and DEFRA is to have improvements in the data, with the appropriate tools to manage it within a reasonable timeframe. Already work through DEFRA’s Broad Scale Modelling research, which ties in closely with the developing Catchment Flood Management Plans, is seeking to put such tools in place. Closely paralleling this work is the construction of the National Flood and Coast Defence Database which too should form a basis for providing consistent data and analyses at a local and strategic level.

# REFERENCES

- MAFF (2000), Assessment of Economic Value of National Assets at Risk from flooding and Coastal Erosion, Project report on Commission FD1702, MAFF.

- Burgess K A, Chatterton J B, Samuels P G, Penning-Rowsell E & Deakin R (2000), Assessment of Economic Value of National Assets at Risk from flooding and Coastal Erosion.

- HR (1999) Wave climate change: Indications from simple GCM outputs, Report TR 80.

- Bürger G, (2000), Expanded downscaling for generating precipitation scenarios, Paper presented at the European Conference on Advances in Flood Research, PIK, Potsdam, Germany, Sept.

- Naden P, Crooks S & Broadhurst P, (1996), Impact of climate and land use change on the flood response of large catchments, paper presented at the 31st MAFF annual conference of river and coastal engineers, MAFF London.

- Calver A, Lamb R & Morris S E (1999), River flood frequency using continuous simulation modelling, Proc ICE, Water Maritime & Energy, Vol 136, pp 225-234

- Samuels P G, (2001), The European River Flood Occurrence and Total Risk Assessment System, Paper 11.1 to be presented at the 36th MAFF annual conference of river and coastal engineers, MAFF London.

- NERC, (1975), Flood Studies Report, Natural Environment Research Council, London (5 Volumes)

- CEH, (2000), Flood Estimation Handbook, Centre of Ecology and Hydrology, Wallingford, Oxon (5 Volumes)

- Hulme M. and Jenkins G J, (1998), Climate change scenarios for the UK: scientific report, UKCIP Technical Report No. 1, Climate Research Unit, University of East Anglia, Norwich, 80pp.

- DETR, (2001), Planning Policy Guidance Note 25: Development and Flood Risk, Department of the Environment Transport and the Regions, February 2001 (Second Consultation Draft).

Please press enter

# Text boxes

- To move from one fill-in location (field) to another, press TAB, RETURN, UP or DOWN arrow keys unless instructed to do otherwise. Locations may also be selected by clicking on them.