Department for Environment, Food and Rural Affairs	CSG 15

Research and Development

Final Project Report

(Not to be used for LINK projects)

Two hard copies of this form should be returned to: Research Policy and International Division, Final Reports Unit DEFRA, Area 301 Cromwell House, Dean Stanley Street, London, SW1P 3JH. An electronic version should be e-mailed to resreports@defra.gsi.gov.uk

| Project title | Estuary morphology - survey and modelling for managed set-back site |
| --- | --- |

| DEFRA project code | FD1004 |  |
| --- | --- | --- |

| Contractor organisation and location | HR Wallingford Ltd Howbery Park, Wallingford OXON, OX10 8BA |
| --- | --- |

| Total DEFRA project costs | £ 80300 |  |
| --- | --- | --- |

| Project start date | 19/05/94 |  | Project end date | 31/03/02 |
| --- | --- | --- | --- | --- |

Executive summary (maximum 2 sides A4) To tab in this section press the tab key and the Control key together Press the DOWN arrow once to move to the next question.

This project has been fully reported through the Tollesbury group led by CEH Dorset with a final presentation from all partners on 25 March 2002. The project has had two phases: the first from 1994 to 1996 included assessment of the initial breach and flooding and was reported previously, while the second phase includes the post breach monitoring and is reported below.

The HR Wallingford contribution over the duration of the second phase of the project was to carry out measurements and modelling, and to assess changes in the vicinity of the sea defence breach and within Tollesbury Creek. The measurements were undertaken annually according to a pre-determined prgogramme and comprised:

- Bathymetric surveys of Tollesbury Creek and Fleet out to Great Cobb Island

- Aerial surveys of the breach and seaward portion of the set-back site

- Section surveys of the breach.

These surveys were analysed to assess changes over time. Measurable and significant changes were found within the Creek and Fleet, but changes within the setback site near the breach were found to be less than the resolution of the measurement method. As a result reporting concentrated on the Creek changes.

In general, over the entire period June 1994 to November 2001 the whole bathymetric survey area deepened, particularly along Tollesbury Creek and in Tollesbury Fleet.   This deepening has occurred in both subtidal and intertidal areas of the estuary.  The subtidal and lower intertidal areas appear to be affected by the breach while the upper intertidal areas are affected by wave action.  The most significant mechanism on the bed levels in the estuary as a whole appears to be the natural year on year variation in the wave climate.  The estuary appears to have deepened as a whole over the period 1994-1996 and subsequently remained broadly stable.  However, there is some suggestion that Old Hall Creek, to the north of Tollesbury Creek, has not yet stabilised since examination of point measurements and cross-section profiles suggests it appears to be accreting and gradually returning to the depths that existed before the breach occurred in 1994.   At other locations within the estuary there appears to be no significant further deepening in the low water channel or on intertidal areas.

Scientific report (maximum 20 sides A4) To tab in this section press the tab key and the Control key together Press the DOWN arrow once to move to the next question.

Scientific report presented as separate PDF file.

Please press enter

# Text boxes

- To move from one fill-in location (field) to another, press TAB, RETURN, UP or DOWN arrow keys unless instructed to do otherwise. Locations may also be selected by clicking on them.