ANNEX 1
STANDARDS OF PERSONAL PROTECTIVE EQUIPMENT

All harmonised standards that give a presumption of conformity to EU law at the end of the transition period will become ‘designated standards’ by the references being published on GOV.UK. Businesses will be able to use designated standards to provide presumption of conformity with GB law.

Harmonised standards remain the relevant standards for placing goods on the Northern Ireland market where EU rules continue to apply.

Note: All protective clothing should conform to BS EN 13688:2013 ‘Protective Clothing General Requirements’.

		Work Activity	Personal protective equipment and clothing to be provided	Full title of standard
1		Any process or activity involving a reasonably foreseeable risk to the head from falling objects	Head Protection to: / EN 397:2012 + A1:2012	Industry safety helmets
2		When working in areas where circumstances involve a reasonably foreseeable risk to the head from bruising or abrasion	Scalp protection to: / BS EN 812:2012	Industrial bump caps
3		When working in small, fast craft	PAS 028:2002	Marine safety helmets
4		When entering or working in a space or working with machinery or equipment where the noise level exceeds 85dB(A)	Ear Protection to: / BS EN 352-1:2020 / Replacing BS EN 352-1:2002	Hearing protectors.General requirements Ear muffs
			BS EN 352-2:2020 / Replacing BS EN 352-2:2002	Hearing protectors.General requirements– Ear plugs
			BS EN 352-3:2020 / Replacing BS EN 352-3:2002	Hearing protectors. General requirements. Ear muffs attached to head protection and /or face protection devices
			BS EN 458:2016 / Replacing BS EN 458: 2004	Hearing protectors Recommendations for selection, use care and maintenance. Guidance document
			Hearing protection should be provided with consideration to appropriate guidance such as Section 7 of the MCA Code Of Practice for Controlling Risks Due to Noise on Ships published by TSO and MIN588 Amendment 1.
5		Welding and gas cutting	Eye and face protection to: / BS EN 175:1997	Personal Protection Equipment for eye and face protection during welding and allied processes
			BS EN 166:2002 / Replaces BS EN 166:1996 / Correction EN 166:2001	Personal eye protection – Specifications
			BS EN 379:2003+A1:2009 / BS EN 169:2002	Personal eye protection Automatic welding filters. / Personal eye protection. Filters for welding and related techniques. Transmittance requirements and recommended use
			Body protection to / BS EN ISO 11611:2015 / Replacing BS EN 470-1:1995 & BS EN ISO 11611:2007 / Additional protection may be required in some situations (e.g. for particularly intense welding/cutting operations).	Protective clothing for use in welding and allied processes.
6		Any work activity in which there is reasonably foreseeable risk of injury to the eye from particles, fragments or injurious substances	Eye protection to: / BS EN 166:2002 / Replaces BS EN 166:1996 / Correction EN 166:2001	Personal eye protection. Specifications
7		Any work activity involving working in an atmosphere which is likely to be hazardous	Note: The following items should be selected and maintained according to: BS EN 529:2005 / Replacing BS 4275:1997	Respiratory protective devices. Recommendations for selection, use, care and maintenance. Guidance document
	(a)	Protection against nuisance dust, mist, particles and dust of low toxicity.	Disposable respirators conforming to: / BS EN 149:2001+A1:2009	Respiratory protective devices. Filtering half masks to protect against particles. Requirements, testing, marking
			General purpose respirators conforming as appropriate to one of the following:
			BS EN 136:1998	Respiratory protective devices: Full face masks. Requirements, testing, marking
			BS EN 140:1999	Respiratory protective devices: half masks or quarter masks. Requirements, testing, marking
			BS EN 12083:1998	Respiratory protective devices. Filters with breathing hoses (non-mask mounted filters) Particle filters, gas filters and combined filters. Requirements, testing, marking
			BS EN 143:2021 / Replacing BS EN 143:2000	Respiratory protective devices. Particle filters. Requirements, testing, marking
			BS EN 14387:2021 / Replacing BS EN 14387:2004+A1:2008	Respiratory protective devices, Gas filter(s) and combined filter(s). Requirements, testing, marking
			BS EN 1827:1999+A1:2009	Respiratory protective devices. Half masks without inhalation valves and with separable filters to protect against gases or gases and particles or particles only. Requirements, testing, marking
	(b)	Protection against toxic dusts and gases of low toxicity	Respirators conforming as appropriate to one of the following:
			BS EN 136:1998	Respiratory protective devices. Full face masks. Requirements, testing, marking
			BS EN 140:1999	Respiratory protective devices. Half masks and quarter masks. Requirements, testing, marking
			BS EN 143:2021 / Replacing BS EN 143:2000	Respiratory protective devices. Particle filters. Requirements, testing, marking
			BS EN 14387:2021 / Replacing BS EN 14387:2004+A1:2008	Respiratory devices. Gas filter(s) and combined filter(s). Requirements, testing, marking
			BS EN 405:2001+A1:2009	Respiratory protective devices. Valved filtering half masks to protect against gases or gases and particles Requirements, testing, marking
			Note: Particulate filters may be incorporated for some applications.
	(c)	Protection against toxic dust	Powered dust respirators, powered dust hoods conforming as appropriate to one of the following:
			BS EN 136:1998	Respiratory protective devices. Full face masks. Requirements, testing, marking
			BS EN 143:2021 / Replacing BS EN 143: 2000	Respiratory protection devices. Particles filters. Requirements, testing, marking
			BS EN 12942: 1998+A2: 2008	Respiratory protective devices. Power assisted filtering devices incorporating full face masks, half masks or quarter masks. / Requirements, testing, marking
			BS EN 12941: 1998+A2:2008	Respiratory protective devices. Powered particle filtering devices incorporating a helmet or hood. Requirements, testing, marking
			Protection against highly toxic atmospheres; or where there is oxygen deficiency; or where there is an alternative to the items above where suitable
	(d)	Protection against highly toxic atmospheres; or where there is oxygen deficiency; or where there is an alternative to the items above where suitable	Breathing apparatus conforming to:
			BS EN 1146: 2005	Respiratory protective devices. Self-contained open circuit compressed air breathing apparatus incorporating a hood for escape. Requirements testing, marking
			BS EN 137:2006	Respiratory protective devices. Self- contained open-circuit compressed air breathing apparatus with full mask. / Requirements, testing, marking
			BS EN 138: 1994 / EN 142:2002	Respiratory protective devices. Specification for fresh air hose breathing apparatus for use with full face mask, half mask or mouth piece assembly.
			BS EN 14593-1:2018 / Replacing: BS EN 14593-1:2005	Respiratory protective devices. Compressed air line breathing devices with demand valve. Devices with a full face mask. / Requirements, testing marking
			BS EN 14593-2:2005 / Replacing: EN 139:1995	Respiratory protective devices. Compressed air line breathing apparatus with demand valve. Apparatus with a half mask / Requirements, testing, marking
			BS EN 14594:2018 / Replacing: BS EN 14594:2005	Respiratory protective devices. Continuous flow compressed air line breathing devices. / Requirements, testing, marking
			BS EN 269: 1995	Respiratory protective devices. Specification for powered fresh air hose breathing apparatus incorporating a hood
			BS EN 402: 2003	Respiratory protective devices. Lung governed demand self- contained open-circuit compressed air breathing apparatus with full face mask or mouthpiece for escape. / Requirements, testing, marking
8		Any process or activity involving working in an area where there is a foreseeable risk of injury from substances which are corrosive or likely to be absorbed through the skin	Protective overalls, gloves or head gear, whichever is appropriate:
			BS EN ISO 13688:2013 / Replacing EN 340:2003	Protective clothing general requirements
			BS EN 14605:2005+A1:2009 / Replacing: / EN 465:1995; / EN 466-1:1995 & / EN 467:1995	Protective clothing against liquid chemicals. Performance requirements for chemical protective clothing with liquid tight (Type 3) or spray-tight (Type 4) connections including items providing protection to parts of the body only (Types PB [3] and PB [4]
			BS EN 943-1:2015+A1:2019	Protective clothing against dangerous solid, liquid and gaseous chemicals, including liquid and solid aerosols - Performance requirements for Type 1 (gas-tight) chemical protective suits
			BS EN 943-2:2019	Protective clothing against dangerous solid, liquid and gaseous chemicals, including liquid and solid aerosols - Performance requirements for Type 1 (gas-tight) chemical protective suits for emergency teams (ET)
9		Any process or activity involving a reasonably foreseeable risk of injury to the hands unless the use of hand protection would increase the risk	Hand protection conforming as appropriate to:
			BS EN 374-1: 2016+ A1 :2018 / Replacing: EN 374-1:2003	Protective gloves against dangerous chemicals and micro-organisms. Terminology and performance requirements for chemical risks
			BS EN 374-2:2019 / Replacing: BS EN 374-2:2014	Protective gloves against dangerous chemicals and micro-organisms. Determination of resistance to penetration
			BS EN 16523-1:2015+ A1:2018 / Replacing: BS EN 374-3:2003	Determination of material resistance to permeation by chemicals. Permeation by potentially hazardous liquid chemicals under conditions of continuous contact
			BS EN ISO 374-4:2019 / Replacing: BS EN 374-4:2013	Protective gloves against dangerous chemicals and mirco-organisms. Determination of resistance to degradation by chemicals.
			BS EN ISO 374-5:2016	Protective gloves against dangerous chemicals and micro- organisms. Terminology and performance requirements for micro-organisms risks.
			BS EN 388:2016+A1:2018 / EN 388:2016+A1:2018 / Replacing: BS EN 388: 2003	Protective gloves against mechanical risks
			BS EN 407:2020 / Replacing: BS EN 407:2004	Protective gloves and other hand protective equipments against thermal risks (heat and/or fire)
			BS EN 510:2019	Specification for protective clothing for use where there is a risk of entanglement with moving parts
			BS EN ISO 21420:2020 / Replacing: BS EN 420:2003+A1:2009	Protective gloves. General requirements and test methods
			BS EN 511:2006 / Replacing: BS EN 511:1994	Protective gloves against cold
10		Any process or activity involving particular risk of injury to the feet	Foot protection conforming to:
			BS EN ISO 20345:2011 / Replacing BS EN ISO 20345:2004	Personal protective equipment. Safety footwear
			BS EN ISO 17249:2013	Safety footwear with resistance to chain saw cutting
			BS EN ISO 15090:2012	Footwear for firefighters
			BS EN ISO 20346:2014	Personal protective equipment. Protective footwear
			BS EN ISO 20347:2012	Personal protective equipment. Occupational footwear
11		Work at height or in any other area where there is a reasonably foreseeable risk of falling	Safety harness and associated lanyard conforming to the following:
			BS EN 353-1:2014 +A1:2017 / Replacing EN 353-1:2014	Personal fall protection equipment. Guided type fall arresters including an anchor line. Guided fall type arresters including a rigid anchor line
			BS EN 353-2:2002	Personal protective equipment against falls from height. Guided type fall arresters including a flexible anchor line
			BS EN 354:2010	Personal fall protection equipment. Lanyards
			BS EN 355:2002	Personal protective equipment against falls from a height. Energy absorbers
			BS EN 358:2018	Personal protective equipment for work positioning and prevention of falls from a height – Belts and lanyards for work positioning or restraint
			BS EN 360: 2002*	Personal protective equipment against falls from height. Retractable type fall arresters
			BS EN 361:2002*	Personal protective equipment against falls from height. Full body harnesses
			BS EN 362:2004*	Personal protective equipment against falls from height. Connectors
			*See BS EN 365:2004 for marking requirements.	Personal protective equipment against falls from a height. General requirements for instructions for use, maintenance, periodic examination, repair, marking and packaging
			BS 8437:2005+A1:2012	Code of Practice for selection, use and maintenance of personal fall protection systems and equipment for use in the workplace
			Or where the use of portable ladders is necessary, such ladders to be used in conjunction with the guidance contained in Chapter 17 in the Code of Safe Working Practices for Merchant Seafarers.
12		Any work carried out from an overside position or in an exposed position where there is a reasonably foreseeable risk or falling or being washed overboard or any work carried out in or from a ship’s boat	Either a MCA approved lifejacket or a personal flotation device conforming as appropriate to one of the following, taking into account the area of operation.
			BS EN ISO 12402-8:2020 / Replacing BS EN ISO 12402-8:2006+A1:2011	Personal flotation devices. Accessories. Safety requirements and test methods
			BS EN ISO 12402-3:2020 / Replacing BS EN ISO 12402-3:2006+A1:2010	Personal flotation devices. Lifejackets, performance level 150. Safety requirements
			BS EN ISO 12402-2:2020 / Replacing: BS EN ISO 12402-2:2006+A1:2010	Personal flotation devices. Lifejackets, performance level 275. Safety requirements
			Partially inherent lifejackets must have at least 89 N of inherent buoyancy; and with the inflatable sections relying on automatic inflation / Specific to the fishing industry only, guidance has been provided within MGN 588 (F) 7.3 Other types of PPE, determined on the basis of a risk assessment.
13		Any work activity where it is necessary to carry out repair or maintenance work on or near exposed live electrical equipment, and there is a reasonably foreseeable risk of injury	Rubber gloves conforming to: BS EN 60903:2003	Live working. Gloves of insulating material
			Protective sleeves conforming to: BS EN 60984:1993	Specification for sleeves of insulating material for live working
			An insulating mat (except where specially insulated flooring is installed) conforming to: / BS EN 61111:2009 / Withdrawn BS 921:1976	Live working. Electrical insulating matting
			BS EN 50321-1:2018	Live working. Footwear for electrical protection - Insulating footwear and overboots
			BS EN 61482-2:2020	Live working. Protective clothing against the thermal hazards of an electric arc - Requirements
			Rubber soled footwear (no standard necessary)
			Note: gloves, sleeves and mats should protect against the appropriate voltage.
14		Any work activity involving a reasonably foreseeable risk of injury from vehicle movement e.g. during ro-ro operations	BS EN ISO 20471:2013+A1:2016 / Replacing: BS EN ISO 20471:2013	High visibility clothing. Test methods and requirements
15		Any work process involving exposure to heat	BS EN ISO 11612:2015 / Replacing BS EN 531:1995	Protective clothing. Clothing to protect against heat and flame. Minimum performance requirements
16		Any work process involving exposure to cool or cold conditions	BS EN 14058:2017 / Replacing BS EN 14058: 2004	Protective clothing. Garments for protection against cool environments
17		Work in engine rooms, machinery spaces or anywhere there is a foreseeable risk of fire or explosion.	BS EN ISO 11612:2015	Protective clothing. Clothing to protect against heat and flame. Minimum performance requirements / Overalls made of fabric of low flammability (e.g. natural fibres, high cotton content) and with / Flame retardant finishes. / Cotton or cotton polyester clothing with flame-retardant finishes are available to protect against sparks and flame