This publication has been withdrawn
The Environment Agency has removed the requirement to consider climate change adaptation from the permit application process. Instead, you need to integrate climate change adaptation into your management system. Use the industry sector examples for your risk assessment when you do this.
Climate change risk assessment worksheet: completed example (based on the south west river basin district)
Potential changing climate variable	A Impact	B Likelihood	C Severity	D Risk (B x C)	E Mitigation (what you'll do to mitigate this risk)	F Likelihood (after mitigation)	G Severity (after mitigation)	H Residual risk (F x G)
1. Summer daily maximum temperature may be around 7°C higher compared to average summer temperatures now.	Ventilation system unable to maintain optimum temperature within livestock housing.	3	3	9	Keep a log of any hot days which occur each year. Install additional cooling system and upgrade building insulation.	3	1	3
2. Winter daily maximum temperature could be 4°C more than the current average, with the potential for more extreme temperatures, both warmer and colder than present.	No negative impact expected.	1	1	1	No mitigation required as very low risk. Score under 5.	1	1	1
3. The biggest rainfall events are up to 20% more intense than current extremes (peak rainfall intensity)*.	a) Effluent treatment plant may require more capacity or careful management. b) Surface water drainage system overloaded. c) Wash-out of fines into watercourse. d) Overtopping of bunds.	a) 3 b) 3 c) 2 d) 2	a) 4 b) 2 c) 2 d) 2	a) 12 b) 6 c) 4 d) 4	a) Increase leachate storage capacity. b) Consider surface falls at design stage. c) Drains and lagoons managed. d) The surface water management plan will need to take increases into consideration. / e) Prepare flood plan with reference to additional guidance “Preparing for flooding. A guide for sites regulated under EPR and COMAH (June 2015)”	a)3 / b)2	a)2 / b)2	a)6 / b)4
4. Average winter rainfall may increase by 41% on today’s averages.	Surface water drainage system overloaded.	3	2	6	Increase surface water storage capacity. Also, as above.	2	2	4
5. Sea level could be as much as 0.6m higher compared to today’s level*.	Inland site. Low impact expected.	3	2	6	Monitor permanent change to local river levels and plan for flood defences as appropriate	2	1	2
6. Drier summers, potentially up to 45% less rain than now.	Increased dust – less water to suppress.	4	2	8	Increase surface water storage capacity (will also help mitigate higher rainfall).	4	1	4
7. The flow in the watercourses could be 40% more than now at its peak*, and 80% less than now at its lowest.	At low flow increased stress on the river at discharge point.	3	2	6	Manage the discharge flow rate to avoid impacts.	2	1	2

*Indicates data has come from climate change allowances as part of the spatial planning process. Evidence from your planning submission is acceptable evidence for this worksheet.