Solar Scoping Table
Examples of information that may be used to support scoping of common matters out of EIAs for solar NSIP developments
Aspect	Matter	Example information to support scoping aspect / matter out of the EIA where relevant
Air quality	Vehicle emissions and dust on human receptors	Evidence/assumptions to be provided in the EIA scoping request / anticipated number, type of vehicle movements, and vehicle routing for all phases / anticipated duration of activities (including earthworks) / typical plant and non-road mobile machinery to be used and expected locations for all phases / location and characterisation of roads that construction traffic is to be routed along / identification of the locations of any sensitive receptors (such as air quality management areas) / likelihood of exceedance of relevant thresholds set out in the appropriate guidance on the need to undertake an assessment of effects (such as Institute of Air Quality Management (IAQM) guidance) / Proposed mitigation to be summarised in the commitments register / dust management measures set out in a draft control document / traffic management measures set out in draft control document / buffer zones and / or screening
Biodiversity	Invasive non-native species (INNS)	Evidence/assumptions to be provided in the EIA scoping request / risk analysis as to whether INNS species are likely to be present / anticipated components and activities of the proposed development across all phases which could result in the introduction and, or spread of invasive species, such as translocation via vehicle movements, water, vegetation management / summary of site surveys or provision of preliminary ecological appraisal, phase one habitat surveys or individual habitat or species surveys / Proposed mitigation to be summarise in the commitments register / Outline of standard measures to identify and control invasive species and how these will be secure, such as through an invasive species management plan
	Species or habitats	Evidence/assumptions to be provided in the EIA scoping request / a preliminary ecological appraisal and / or phase one habitat survey completed within the two years prior to submission of the scoping request / Identification, location, importance and sensitivity of species/habitats within a Zone of Influence (ZoI) with reference to relevant guidance to define sensitivity of species/habitats on site/ potential to be on site / evidence of absence of suitable supporting habitat for a particular species / Proposed mitigation to be summarise in the commitments register / commitment to any anticipated follow up surveys required / appropriate buffers / construction management measures / any proposed strategic level licencing processes that will be relied upon, for example district level licencing for great crested newts
Climate Change	Exacerbation of, and resilience to, climate change effects	Evidence/assumptions to be provided in the EIA scoping request / description of potential climate change impacts both now and in the future, considering both the lifetime of the Proposed Development and appropriate future climate change projections, such as tidal reach and flooding from the sea/coastal erosion, surface and fluvial flood risk / Proposed mitigation to be summarise in the commitments register / a commitment to design measures that ensure climate resilience, for example location and height of panels above existing and future flood levels
Human Health	Vehicle emissions and dust	Please see the relevant section in this table under ‘Air quality’. Where this is proposed to be scoped out of an assessment to Human Health, this should either include the relevant information set out under ‘Air Quality’ or appropriately cross reference to where this is discussed in the scoping request.
	Noise and vibration	Please see the relevant section in this table under ‘Noise and vibration’. Where this is proposed to be scoped out of an assessment to Human Health, this should either include the relevant information set out under ‘Noise and Vibration’ or appropriately cross reference to where this is discussed in the scoping request.
Land and Soils	Contaminated Land	Evidence/assumptions to be provided in the EIA scoping request / description of anticipated installation methods and locations for foundations of panels, for example concrete ballast, piling / anticipated location of battery storage / description of underlying geology, hydrology, hydrogeology or ground conditions that may affect the mobilisation and movement of contaminant with reference to relevant desk studies or surveys / A review of known historical land uses and likelihood of sources of contamination being present with reference to relevant desk studies or surveys where available / Technical assessment to be provided with the application / a phase one contaminated land report / Proposed mitigation to be summarise in the commitments register / commitment to providing: / drilling fluid breakout plan / emergency spill response procedure / battery safety management plan / appropriate buffers / construction management measures / best practice measures during each phase to reduce risk of contaminant mobilisation
	Minerals	Evidence/assumptions to be provided in the EIA scoping request / description of anticipated mineral deposits likely to present / affected and any safeguarding zones informed by either desk studies, surveys or consultation with the relevant Minerals Planning Authorities / anticipated lifetime of the proposed development / anticipated interactions with mineral deposits where they are likely to be present, and a conclusion on the potential sterilisation of land for mineral extraction / Proposed mitigation to be summarise in the commitments register / measures to mitigate impacts to minerals, for example reduction in the area and amount of resource impacted, extraction in advance of development where there is the potential for sterilisation / to gain agreement with the Minerals Planning Authority that that the proposed development would not impact on plans for minerals extraction within the region
Major Accidents and Disasters		Evidence/assumptions to be provided in the EIA scoping request / explanation as to how potential major accident and disaster risks have informed the site selection and the proposed development description in the scoping request / A major accident and disaster risk identification screening exercise, taking into consideration the potential consequence and anticipated likelihood of occurrence, with consideration given to any relevant thresholds for significance identified within industry guidance, for example battery fire / Identification of any sensitive receptors in relation to the site including for example Control of Major Accident Hazards Regulations (COMAH) sites / Proposed mitigation to be summarise in the commitments register / commitment to providing, or provision of plans to manage risks identified in the scoping request, for example drainage strategy, outline construction environmental management plan (OCEMP), battery safety management plan
Noise and Vibration	Construction, operation and decommissioning	Evidence/assumptions to be provided in the EIA scoping request / anticipated noise generating activities and locations during each phase of the development, for example piling, removal of piles, trenching, if tracker panels are proposed / anticipated maximum duration of construction activities and timing across all phases / anticipated plant and non-road mobile machinery types for all phases / vehicle routing including access locations (where known) / vehicle type and number of movements for all phases / likelihood of exceedance of relevant thresholds set out in the appropriate guidance on the need to undertake an assessment of effects (for example Institute of Environmental Management and Assessment (IEMA) guidance) / identification of the locations of any sensitive receptors / Proposed mitigation to be summarise in the commitments register / best practice noise management measures set out in a draft OCEMP, Outline Operational Environmental Management Plan (OOEMP) and Outline Decommissioning Environmental Management Plan (ODEMP) / buffer zones and/ or screening measures
Traffic and Transport	Road vehicle driver and passenger and non-motorised user delays, fear and intimidation, road user and pedestrian safety and hazardous/large loads	Evidence/assumptions to be provided in the EIA scoping request / anticipated vehicle movements, type and duration / anticipated vehicle routing and access / whether alternative transport will be used, for example canal, railway / characterisation of the local road network and existing traffic movements, for example quiet rural roads or busy strategic network, existing congestion issues, any weight or height restrictions / likelihood of exceedance of relevant thresholds set out in the appropriate guidance on the need to undertake an assessment of effects (for example IEMA guidance) / Proposed mitigation to be summarise in the commitments register / commitment to provide construction traffic management plan (CTMP) to secure the number of vehicle movements, vehicle type, routing and access. This should include measures such as safe transport of large loads, routing away from sensitive receptors where possible/relevant, temporary diversions, traffic lights, other relevant road safety measures
Waste	Construction	Evidence/assumptions to be provided in the EIA scoping request / anticipated waste streams and quantities / Proposed mitigation to be summarise in the commitments register / commitment to provide a waste management plan including: / best practice measures / Demonstration of adherence to the waste hierarchy / Appropriate monitoring measures to ensure compliance
Water environment	Ground and surface water quality	Evidence/assumptions to be provided in the EIA scoping request / identification of water receptors / anticipated impact pathways / Proposed mitigation to be summarise in the commitments register / buffer zones between potentially polluting activities and surface water receptors / commitment to best practice measures in OCEMP / commitment to drainage design measures / commitment to provision of a drilling fluid breakout plan where horizontal directional drilling is proposed / commitment to emergency spill response procedure / commitment to battery safety management plan
	Flood risk	Technical assessment to be provided with the application / commitment to provide a Flood Risk Assessment that will include: / identification of flood risk zones including delineation between flood risk zones 3a and 3b / separate section to demonstrate the sequential test has been met (where required) / separate section to demonstrate the exception test has been met (where required) / description of a sustainable drainage scheme / description of measures to provide floodplain storage where 3b is impacted / confirmation that a significant effect would not result from any type of flood risk (for example surface, fluvial, groundwater), either to or from the development, when taking into account relevant climate change factors