# Site investigation permits
This guidance tells you what supporting information you need to provide when applying for a permit for site investigation work that may intersect mine workings or mine entries. This checklist covers the standard information required for this activity. Please provide any other relevant site specific information not included here.
### Before you apply
If you are drilling any borehole of 30 metres depth or more in a mining area, you must send a Borehole Site and Operations Regulations notification to the Health and Safety Executive. This is a requirement under Regulation 6(3) of Borehole Site and Operations Regulations 1995. Health and Safety Executive has published further guidance at A guide to the Borehole Sites and Operations Regulations 1995. Guidance on Regulations - HSE
## Site investigation of mine workings
### CAD drawings (or similar standard)
Your drawing on an Ordnance Survey base map must show:
- a red boundary identifying all land where permitted activities will take place
- if using angle or directional drilling, the land over which angle drilling will take place
- ground investigation locations, individually labelled or numbered with a unique reference and type indicated (for example, BH101RC or RC101)
- geotechnical constraints including mining features and zones of collapse
### Supporting information
You must provide:
- schedule of borehole coordinates (in spreadsheet format if possible)
- desk study report, which may include mining plans
details of controls to deal with gas and water under pressure for boreholes that are 30 metres deep or more
- geotechnical constraints and specification
- receptor information
## Site investigation of mine entries by excavation or probe drilling
### CAD drawings (or similar standard)
Your drawing on an Ordnance Survey base map must show:
- a red boundary identifying all land where permitted activities will take place
- if using angle or directional drilling, the land over which angle drilling will take place
- probing locations, individually labelled or numbered with a unique reference
- geotechnical constraints including mining features and zones of collapse
- a detailed plan showing trenching details such as trench width, length, depth and spacing of any excavations proposed
- notes detailing protection measures and reinstatement
### Supporting information
You must provide:
- schedule of probe hole coordinates (in spreadsheet format if possible)
- details of controls to deal with gas and water under pressure for boreholes that are 30 metres deep or more
- desk study report, which may include mining plans
- geotechnical constraints and specification
- receptor information
## Site investigation for deep boreholes
### CAD drawings (or similar standard)
Your drawing on an Ordnance Survey base map must show:
- a red boundary identifying all land where permitted activities will take place
- if using angle or directional drilling, the land over which angle drilling will take place
- subsurface horizons showing any known subsurface structures (mining-related or geological) obtained by research or technical surveys, where relevant to the proposed boreholes
### Supporting information
You must provide:
- schedule of probe hole coordinates (in spreadsheet format if possible)
- desk study report, which may include mining plans
- anticipated geology and target horizons
- details of controls to deal with gas and water under pressure
- reason for the chosen depth of borehole
- geotechnical constraints and specification, including casing details
- receptor information