# Site remediation using concrete capping and geotextiles
This guidance tells you what supporting information you need to provide when applying for a permit for mine entry protection measures, including reinforced concrete capping, geotextiles, and retention of existing protection. This checklist covers the standard information required for this activity. Please provide any other relevant site specific information not included here.

## Reinforced concrete capping of mine entry
### CAD drawings (or similar standard)
Your detailed drawings of the proposed cap construction must be in plan view and elevation and show:
- existing infrastructure and structures (such as drainage and sustainable drainage systems) within the zone of influence
- rockhead identified, or a profile of superficial deposits if not founded on rockhead
- any structures, buildings and infrastructure (such as drainage or highway) within the zone of influence of the shaft, existing or proposed
- full dimensions of the shaft cap
- full details and dimensions of the reinforcement
- existing and proposed ground levels clearly identified
- details of bearing arrangement
- details of any special foundation arrangement such as trench fill

### Supporting calculations
You must provide calculations that show:
- there is adequate bearing capacity of the founding strata, based on ground investigation data (refer to Section 6 of our technical guidance note TGN02/2021)
- the structural design of the cap is fit for purpose
- the pile design, if a piled shaft cap is proposed
- loading assessment provided to BS EN 1991 or equivalent standard, demonstrating how design actions have been derived
- loading assessment to BS EN 1991-2:2003 or equivalent standard, where the cap is subject to highway loading

### Investigation and design reports
Your reports must include:
source information on which the design has been based, such as the ground investigation report and ground model
records of previous shaft investigations and treatments, particularly where shaft caps are not located at rockhead
## Geotextiles as a final treatment of a mine entry
### CAD drawings (or similar standard)
Your detailed drawings of the proposed construction sequence showing geotextile and superficial deposit must be in plan view and elevation and show:
- existing infrastructure and structures (such as drainage and sustainable drainage systems) within the zone of influence
- rockhead identified, or a profile of superficial deposits if not founded on rockhead
- any structures, buildings and infrastructure (such as drainage or highway) within the zone of influence of the shaft, existing or proposed
- full dimensions of the geogrid, with type and model annotated
- existing and proposed ground levels clearly identified
### Design document
Your design document must demonstrate the chosen geogrid is fit for purpose and include:
- manufacturer's data sheet or specification document
- calculations showing the design has been carried out to an appropriate British Standard (such as BS 8006)
- evidence the design life is sufficient for the authority's requirements
- confirmation parameters used are derived from the supporting ground investigation information
- the overburden loading (soils only)
### Investigation and design reports
Your reports must include:
- source information on which the design has been based, such as the ground investigation report and ground model
- records of previous shaft investigations and treatments, particularly where shaft caps are not located at rockhead

## Retention of existing protection measures
### CAD drawings (or similar standard)
Your detailed drawings of the existing cap construction must be in plan view and elevation and show:
- existing infrastructure and structures (such as drainage and sustainable drainage systems) within the zone of influence
- rockhead identified, or a profile of superficial deposits if not founded on rockhead
- any structures, buildings and infrastructure (such as drainage or highway) within the zone of influence of the shaft, existing or proposed
- full dimensions of the shaft cap
- full details and dimensions of the existing reinforcement
- existing and proposed ground levels clearly identified
- details of any special foundation arrangement such as trench fill
### Back analysis calculations
You must provide calculations that show:
- there is adequate bearing capacity of the founding strata, based on ground investigation data (refer to Section 6 of our technical guidance note TGN02/2021)
- the existing shaft cap is constructed to a sufficient standard and is fit for the proposed purpose
- a loading assessment of the existing cap to BS EN 1991, demonstrating how design actions have been derived
- a loading assessment to BS EN 1991-2:2003, where the cap is subject to highway loading
### Investigation and design reports
Your reports must include:
- source information on which the design has been based, such as the ground investigation report and ground model
- records of previous shaft investigations and treatments, particularly where shaft caps are not located at rockhead
- detailed report of the investigation data used in the back analysis, such as coring logs, laboratory determination of core strength, reinforcement measurement and assessment
- clarification if data is as-built or new data