NOTE: To be completed by ‘competent’ persons with current knowledge of conducting noise assessments. This form is not suitable for assessing impulse noise from military weapons, explosives and pyrotechnics which should be assessed by a specialist with a bespoke risk assessment.

Assessment details
Establishment / Unit / Platform:					Section / Department / Sub-unit:
Location of assessment (address)					Type of noise environment
					Continuous ☐ Impulsive ☐
MOD Form 5017 Reference No.					Main risk assessment (MOD Form 5010) Reference No.

Assessment carried out by
Assessor name:					Signature: (only if form is completed by hand)
Post / Role:					Rank / Grade:					Date:

Summary of results (complete after sections 4 – 10)
Post (name)					Number of / personnel / exposed	Lower Exposure / Action Value reached?					Upper Exposure / Action Value / reached?					Exposure Limit Value / reached? / (Hearing protection / accounted for)
					LEP,d 80 dB(A)			LCpeak 135 dB(C)		LEP,d 85 dB(A)		LCpeak 137 dB(C)				LEP,d 87 dB(A)		LCpeak 140 dB(C)
					☐			☐		☐		☐				☐		☐

Is a specialist noise assessment or advice required due to presence of impulse noise or Exposure Limit Values exceeded with mitigation? (LEP,d over 100 dB(A)) Yes ☐ No ☐

Measurement details

Measurement equipment
Sound level meter		Serial No.		Date of calibration
Microphone		Serial No.		Date of calibration
Calibrator model		Serial No.		Date of calibration

Description / sketch / images of area covered by the assessment / (Identify locations of noise sources, normal working positions, etc)

Details of operations / remarks / (Detail the work / activities undertaken, and any control measures currently in place)

Measurement results					Hearing Protection
Start calibration level (dB)				End calibration check (dB)					Make / model:
Activity / (as specified in / section 6)	Measurement			Activity Noise Exposure					In use currently?	Yes ☐ No ☐
				SNR:
	Duration	LAeq,t / dB(A)	LCeq,t / dB(C)	Activity Duration	LAeq dB(A)	Exposure / Points		LCeq / dB(C)	LCpeak / dB(C)	L’Aeq at the ear (LCeq–SNR+4) dB(A)	Exposure / Points / at the ear

				Total / points					Total / points
				LEP,d / no hearing / protection					L’EP,d / with hearing / protection

Recommendations
Actions necessary to comply with JSP 375 Volume 1, Chapter 25 - Noise at work
Reduction of noise exposure by means other than the provision of hearing protection / (Essential if personnel are exposed at / or above the Upper Exposure Action Value)

Information, Instruction, and Training of personnel / (Essential if personnel are exposed at or above the Lower Exposure Action Value)

Hearing Protection Zones / (Essential in all areas where personnel are exposed at or above the Upper Exposure Action Value)

Provision of personal hearing protection / (Where applicable, is the current hearing protection suitable and sufficient, or is additional / alternative hearing protection required? Include types and NATO Stock numbers, where possible)

Additional recommendations / (List any further actions which have not been previously discussed)

Further comments

Action taken by commander, manager or accountable person

Name:					Signature (only if form is completed by hand)
Post / Role:					Rank / Grade:					Date:

Record of reviews
Note: A review should be undertaken at a frequency that is appropriate to the level of risk of the particular activity (e.g., high risk - potentially each time the activity is to be conducted or at least 6 monthly; medium risk review control measures and improve if reasonably practicable to do so (6 monthly or at least annually); low risk – annually), or if there is a change in work practices, equipment or personnel.
Date of initial assessment					Reference No. of initial assessment

Date of review		Name of reviewer					Grade / Rank					Re-assess?
					☐
					☐
					☐

If a re-assessment is required, please fill in a new Noise Assessment Record and enter the details below.
Reference No. of new assessment					Date of new assessment

Above upper exposure action value (LEP,d 85 dB(A))
Above lower exposure action value (LEP,d 80 dB(A))
Below lower exposure action value (LEP,d 80 dB(A))

Table 1 – MOD - Noise exposure ready-reckoner (daily exposure)
Instructions:
1. For each task or period of noise exposure in the working day look up in the table on the left the exposure points corresponding to the sound pressure level and duration (e.g. exposure to 93 dB(A) for 1 hour gives 80 exposure points);
2. Add up the points for each task or period to give total exposure points for the day;
3. Look up in the table on the right the total exposure points to find the corresponding daily noise exposure (e.g. a total exposure points for the day of 280 points gives a daily noise exposure of between 89 dB(A) and 90 dB(A)).